## Slide 1: CS107 Lecture 17 Assembly: Arithmetic and Logic Wrap, Control Flow
Reading: B&O 3.5-3.6

## Slide 2: Multiplication Support
Multiplying 64-bit numbers can produce 128-bit results. How does x86-64 support this with only 64-bit registers?
If you specify two operands to imul or mul, it multiplies them and truncates the result to fit in the second of the two.
imul S, D is realized as D ← D * S
If you specify one operand, it’s multiplied by %rax and the product is split across two registers: the high-order 64 bits go in %rdx and the low-order 64 bits in %rax.
Instruction | Effect | Description
imulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Signed full multiply
mulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Unsigned full multiply

## Slide 3: Division and Mod Support
x86-64 supports dividing a 128-bit value by a 64-bit value.
The high-order 64 bits of the dividend need to be prepared and stored in %rdx, the low-order 64 bits in %rax. The divisor is the only listed operand.
The integer quotient is stored in %rax, and the remainder in %rdx.
Most dividend are just 64-bit. The cqto instruction sign-extends the 64-bit value in %rax though %rdx to fill both registers with the dividend, as idiv and div expect.
Instruction | Effect | Description
idivq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Signed divide
divq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Unsigned divide
cqto | R[%rdx]:R[%rax] ← SignExtend(R[%rax]) | Convert to oct word

## Slide 4: Reverse Engineering Etude
Examine the assembly code emitted on behalf of the three-argument div_and_mod function and reconstruct an equivalent, four-line implementation in C.
div_and_mod:
movq %rdi, %rax
movq %rdx, %rcx
cqto
idivq %rsi
movq %rdx, (%rcx)
ret
long div_and_mod(long x, long y, long *p_mod) {
long quotient = x / y;
long remainder = x % y;
*p_mod = remainder;
return quotient;
}
Assembly:
C:
Key Insights:
The first and third lines of assembly suggest x—delivered via %rdi—is the dividend of the forthcoming division.
The second line stores a copy of p_mod (courtesy of %rdx) in %rcx.
The fourth line divides x by y (supplied via %rsi), populating %rax with the integer quotient and %rdx with the remainder.
  This explains why a copy of p_mod was placed in %rcx—the compiler recognized %rdx would be overwritten by idivq two lines later.
              The remainder is written through the address stored in %rcx, suggesting *p_mod = x % y
              %rax still holds the integer quotient when the function returns, suggesting something akin to return x / y

## Slide 5: Reverse Engineering Etude 1
Examine the assembly code emitted on behalf of the three-argument div_and_mod function and reconstruct an equivalent, four-line implementation in C.
div_and_mod:
movq %rdi, %rax
movq %rdx, %rcx
cqto
idivq %rsi
movq %rdx, (%rcx)
ret
long div_and_mod(long x, long y, long *p_mod) {
long quotient = x / y;
long remainder = x % y;
*p_mod = remainder;
return quotient;
}
Assembly:
C:
Key Insights:
The first and third lines of assembly suggest x—delivered via %rdi—is the dividend of the forthcoming division.
The second line stores a copy of p_mod (courtesy of %rdx) in %rcx.
The fourth line divides x by y (supplied via %rsi), populating %rax with the integer quotient and %rdx with the remainder.
  This explains why a copy of p_mod was placed in %rcx—the compiler recognized %rdx would be overwritten by idivq two lines later.
              The remainder is written through the address stored in %rcx, suggesting *p_mod = x % y
              %rax still holds the integer quotient when the function returns, suggesting something akin to return x / y

## Slide 6: Reverse Engineering Etude
Examine the assembly code emitted on behalf of the three-argument tinker_toy function and complete the implementation.
tinker_toy:
movslq %edx, %rdx
movl %edi, %eax
addl (%rsi,%rdx,4), %eax
ret
int tinker_toy(int x, int arr[], int y) {
int sum = __________; sum += arr[__________]; return __________;
}
Assembly:
C:
Key Insights:
Because the third argument y is an int, it’s really passed in %edx, and the upper half of %rdx is irrelevant garbage.
However, a sign-extended copy of y is placed in %rdx via the first instruction, since the addressing mode of the third line requires full registers. %edx itself doesn’t qualify.
        Because sum is declared as an int and is the focus of the implementation, it’s reasonable to assume sum is backed by %eax and that its final value is what’s returned.
        The second line initializes sum to x, and the third adds arr[y] to sum. Note the scale factor in line three is a 4, and that’s what you’d expect with int * pointer arithmetic.
sum
x
y

## Slide 7: Executing Instructions
So far:
Program values can be stored in memory or in registers.
Assembly instructions read and write values back and forth between registers and main memory.
Assembly instructions are also stored in memory.
Big Questions:
What controls execution flow? How does a process know what instruction to execute next?
Answer:
The program counter, stored in %rip.
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55

## Slide 8: Following %rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Heap
Stack
Data
Text (code)
Main Memory

## Slide 9: Following %rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Heap
Stack
Data
Text (code)
Main Memory
0x4004ed
%rip
In x86-64, %rip serves as the program counter and holds the address of the next instruction to be executed.

## Slide 10: Following %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004ee
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
In x86-64, %rip serves as the program counter and holds the address of the next instruction to be executed.

## Slide 11: Following %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f1
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
In x86-64, %rip serves as the program counter and holds the address of the next instruction to be executed.

## Slide 12: Following %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f8
%rip
In x86-64, %rip serves as the program counter and holds the address of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 13: Following %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
In x86-64, %rip serves as the program counter and holds the address of the next instruction to be executed.

## Slide 14: Following %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
Normally, dedicated hardware sets the program counter to the address of the next instruction:
%rip += current instruction size
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 15: Interrupting Control Flow
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 16: Interrupting Control Flow
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f8
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).

## Slide 17: Interrupting Control Flow
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).

## Slide 18: Interrupting Control Flow
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f8
%rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
The above might reverse compile to:
int n = 0; while (true) n++; ...

## Slide 19: The jmp Instruction
The jmp instruction jumps to another instruction in the assembly code—an unconditional jump.
jmp Label (Direct Jump)
jmp *Operand (Indirect Jump)
The single operand can be encoded directly into the instruction as a direct jump:
jmp 404f8 <loop+0xb>
The operand can be expressed as an indirect jump using one of the many addressing modes
jmp *%rax
Aside: Direct, unconditional jumps are frequently used for loopbacks in for and while loops and for skipping around else blocks.
Another Aside: Indirect unconditional jumps are much less common, used on behalf of very large switch statements and function pointers.
Next Question: What if we want to jump conditionally?