## Slide 1: CS107 Lecture 19 Assembly: Function Call
Reading: B&O 3.7

## Slide 2: Calling Functions In Assembly
To call a function in assembly, we must do a few things:
Transfer Control – %rip must be adjusted to execute the callee’s instructions and then resume the caller’s instructions afterwards.
Pass Data – we must pass parameters and extract return values.
Manage Memory – we must handle the callee’s stack space needs.
Terminology: caller function calls the callee function.
How does assembly interact with the stack?

## Slide 3: Tracking %rsp
%rsp is a special register that stores the address of the current "top" of the stack (the bottom in our diagrams, since the stack grows downwards).
0x0
main()
Heap
myfunction()
Data
Text (code)
%rsp
Main Memory

## Slide 4: Tracking %rsp
%rsp is a special register that stores the address of the current “top” of the stack (the bottom in our diagrams, since the stack grows downwards).
0x0
main()
Heap
myfunction()
Data
Text (code)
%rsp
Main Memory
foo()

## Slide 5: Tracking %rsp
%rsp is a special register that stores the address of the current “top” of the stack (the bottom in our diagrams, since the stack grows downwards).
0x0
main()
Heap
myfunction()
Data
Text (code)
%rsp
Main Memory
foo()
bar()

## Slide 6: Tracking %rsp
%rsp is a special register that stores the address of the current “top” of the stack (the bottom in our diagrams, since the stack grows downwards).
0x0
main()
Heap
myfunction()
Data
Text (code)
%rsp
Main Memory
foo()

## Slide 7: Tracking %rsp
%rsp is a special register that stores the address of the current “top” of the stack (the bottom in our diagrams, since the stack grows downwards).
0x0
main()
Heap
myfunction()
Data
Text (code)
%rsp
Main Memory
Key idea: %rsp must point to the same place before a function is called and after that function returns, since stack frames go away when a function finishes.

## Slide 8: Understanding push and pop
The push instruction pushes the data at the specified source onto the top of the stack, adjusting %rsp accordingly.
Instruction | Effect
pushq S | R[%rsp] ⟵ R[%rsp] – 8; M[R[%rsp]] ⟵ S

## Slide 9: Understanding push and pop
The push instruction pushes the data at the specified source onto the top of the stack, adjusting %rsp accordingly.
Instruction | Effect
pushq S | R[%rsp] ⟵ R[%rsp] – 8; M[R[%rsp]] ⟵ S

## Slide 10: Understanding push and pop
The push instruction pushes the data at the specified source onto the top of the stack, adjusting %rsp accordingly.
Instruction | Effect
pushq S | R[%rsp] ⟵ R[%rsp] – 8; M[R[%rsp]] ⟵ S

## Slide 11: Understanding push and pop
The push instruction pushes the data at the specified source onto the top of the stack, adjusting %rsp accordingly.
This behavior is equivalent to the following, but pushq is a shorter instruction:
subq $8, %rsp
movq S, (%rsp)
Sometimes, you’ll see instructions just explicitly decrement the stack pointer to make room for new local variables.
Instruction | Effect
pushq S | R[%rsp] ⟵ R[%rsp] – 8; M[R[%rsp]] ⟵ S

## Slide 12: Understanding push and pop
The pop instruction pops the topmost data from the stack and stores it in the specified destination, adjusting %rsp accordingly.
Note: this doesn’t remove/clear out the data. It just increments %rsp to indicate the next push can overwrite that location.
Instruction | Effect
popq D | D ⟵ M[R[%rsp]] R[%rsp] ⟵ R[%rsp] + 8;

## Slide 13: Understanding push and pop
The pop instruction pops the topmost data from the stack and stores it in the specified destination, adjusting %rsp accordingly.
This behavior is equivalent to the following, but popq is a shorter instruction:
movq (%rsp), D
addq $8, %rsp
Sometimes, you’ll see instructions just explicitly increment the stack pointer to pop data.
Instruction | Effect
popq D | D ⟵ M[R[%rsp]] R[%rsp] ⟵ R[%rsp] + 8;

## Slide 14: push and pop Etude
Initially | 
%rax | 0x123
%rdx | 0
%rsp | 0x108
Stack “bottom”
Stack “top”
0x108
Increasing
addresses
pushq %rax | 
%rax | 0x123
%rdx | 0
%rsp | 0x108
Stack “bottom”
Stack “top”
Increasing
addresses
popq %rdx | 
%rax | 0x123
%rdx | 0x123
%rsp | 0x100
Stack “bottom”
0x108
Increasing
addresses
0x123
Stack “top”
0x108
0x100
0x100
0x123
0x100
0x108

## Slide 15: Calling Functions In Assembly
To call a function in assembly, we must do a few things:
Pass Control – %rip must be adjusted to execute the callee’s instructions, and then resume the caller’s instructions afterwards.
Pass Data – we must pass any parameters and receive any return value.
Manage Memory – we must handle any space needs of the callee on the stack.
Terminology: caller function calls the callee function.

## Slide 16: Remembering Where We Left Off
Problem: %rip points to the next instruction to execute. To call a function, we must remember that instruction address for later.
Solution: push the next value of %rip onto the stack. Then call the function. When it is finished, put this value back into %rip and continue executing as if never interrupted by the function call.
…
…
Stack
0xff20
%rsp
main()
0x3026
%rip
E.g. main() calls foo():

## Slide 17: Remembering Where We Left Off
Problem: %rip points to the next instruction to execute. To call a function, we must remember that instruction address for later.
Solution: push the next value of %rip onto the stack. Then call the function. When it is finished, put this value back into %rip and continue executing.
…
…
0x3026
Stack
main()
0xff18
%rsp
0x3026
%rip
E.g. main() calls foo():

## Slide 18: Remembering Where We Left Off
Problem: %rip points to the next instruction to execute. To call a function, we must remember that instruction address for later.
Solution: push the next value of %rip onto the stack. Then call the function. When it is finished, put this value back into %rip and continue executing.
…
…
0x3026
…
Stack
main()
foo()
0xff08
%rsp
0x4058
%rip
E.g. main() calls foo():

## Slide 19: Remembering Where We Left Off
Problem: %rip points to the next instruction to execute. To call a function, we must remember that instruction address for later.
Solution: push the next value of %rip onto the stack. Then call the function. When it is finished, put this value back into %rip and continue executing.
…
…
0x3026
Stack
0xff18
%rsp
0x4175
%rip
main()
E.g. main() calls foo():

## Slide 20: Remembering Where We Left Off
Problem: %rip points to the next instruction to execute. To call a function, we must remember that instruction address for later.
Solution: push the next value of %rip onto the stack. Then call the function. When it is finished, put this value back into %rip and continue executing.
…
…
Stack
main()
0xff20
%rsp
0x3026
%rip
E.g. main() calls foo():

## Slide 21: Call And Return
The call instruction pushes the address of the instruction immediately following the call instruction onto the stack and sets %rip to point to the beginning of the specified function’s instructions.
call Label
call *Operand
The ret instruction pops this instruction address from the stack and stores it in %rip.
ret
The stored %rip is called the return address. It is the address of the instruction where execution would have continued had flow not been interrupted by the function call. (Don’t confuse this with return value, which is the value returned by the function via %rax or a subset of it).
Notes: Function pointers!

## Slide 22: Registers
What does call do?
call pushes the next instruction address onto the stack and overwrites %rip to address another function’s very first instruction.

## Slide 23: Registers
What does ret do?
ret pops off the 8 bytes from the top of the stack and places it in %rip, thereby resuming execution in the caller.
ret is separate from the return value of the function (put in %rax).

## Slide 24: Function Pointers
The call instruction pushes the address of the instruction immediately following the call instruction onto the stack and sets %rip to point to the beginning of the specified function’s instructions.
call Label
call *Operand
Why would we use call with a register instead of hardcoding the function name in the assembly? When would we not know the function to call until we run the code?
Function pointers! e.g., qsort – qsort calls a function passed through as a parameter and stored in a register.

## Slide 25: Parameters and Return
There are special registers that store parameters and the return value.
To call a function, we must put any parameters we are passing into the correct registers. (%rdi, %rsi, %rdx, %rcx, %r8, %r9, in that order)
Parameters beyond the first 6 are placed directly on the stack.
If the caller expects a return value, it looks in %rax after the callee completes.

## Slide 26: Local Storage
So far, all local variables have been stored directly in registers.
There are four common reasons that a local variable must be stored in memory instead of a register:
  We’ve simply run out of registers—we only have 16, some of which are special-purpose.
  Not all registers are protected against function calls, so any variables or important partial results stored in registers sometimes need to be flushed out to the stack.
  The & operator is applied to a variable, so we need a true address for it
  The variables themselves are arrays or structs and are better stores on the stack as an aggregate of memory.

## Slide 27: Local Storage
long caller() {
long arg1 = 534;
long arg2 = 1057;
long sum = swap_add(&arg1, &arg2);
...
}
caller:
sub $0x10, %rsp // 16 bytes for stack frame
movq $0x216, 0x8(%rsp) // store 534 in arg1
movq $0x421, (%rsp) // store 1057 in arg2
mov %rsp, %rsi // compute &arg2 as second arg
lea 0x8(%rsp), %rdi // compute &arg1 as first arg
callq swap_add // call swap_add(&arg1, &arg2)

## Slide 28: Parameters and Return
 | ...
main()
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}

## Slide 29: Parameters and Return
 | ...
main()
0xffea08
0x40054f
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40054f <+0>: sub $0x18,%rsp
0x400553 <+4>: movl $0x1,0xc(%rsp)
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 30: Parameters and Return
 | ...
0xffe9f0 | 
main()
0xffe9f0
0x400553
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40054f <+0>: sub $0x18,%rsp
0x400553 <+4>: movl $0x1,0xc(%rsp)
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 31: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f0 | 
main()
0xffe9f0
0x40055b
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40054f <+0>: sub $0x18,%rsp
0x400553 <+4>: movl $0x1,0xc(%rsp)
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 32: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f0 | 
main()
0xffe9f0
0x400563
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40054f <+0>: sub $0x18,%rsp
0x400553 <+4>: movl $0x1,0xc(%rsp)
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 33: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 
main()
0xffe9f0
0x40056b
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400553 <+4>: movl $0x1,0xc(%rsp)
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 34: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
main()
0xffe9f0
0x400572
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40055b <+12>: movl $0x2,0x8(%rsp)
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 35: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
main()
0xffe9e8
0x400574
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400563 <+20>: movl $0x3,0x4(%rsp)
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 36: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x400576
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40056b <+28>: movl $0x4,(%rsp)
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 37: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x40057c
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 38: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x40057c
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>

## Slide 39: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x40057c
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400572 <+35>: pushq $0x4
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
2
%r9d

## Slide 40: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x400582
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400574 <+37>: pushq $0x3
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
2
%r9d
1
%r8d

## Slide 41: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x400587
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400576 <+39>: mov $0x2,%r9d
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
2
%r9d
1
%r8d
0xffe9f0
%rcx

## Slide 42: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x40058c
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40057c <+45>: mov $0x1,%r8d
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx

## Slide 43: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x400591
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400582 <+51>: lea 0x10(%rsp),%rcx
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx
0xffe9f8
%rsi

## Slide 44: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x400596
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x400587 <+56>: lea 0x14(%rsp),%rdx
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
0x40059b <+76>: add $0x10,%rsp
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx
0xffe9fc
%rdi
0xffe9f8
%rsi

## Slide 45: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
main()
0xffe9e0
0x40059b
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
0x40059b <+76>: add $0x10,%rsp
…
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx
0xffe9fc
%rdi
0xffe9f8
%rsi

## Slide 46: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
 | 0x40059b
main()
0xffe9d8
0x40059b
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
0x40059b <+76>: add $0x10,%rsp
…
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx
0xffe9fc
%rdi
0xffe9f8
%rsi

## Slide 47: Parameters and Return
 | ...
0xffe9fc | 1
0xffe9f8 | 2
0xffe9f4 | 3
0xffe9f0 | 4
0xffe9e8 | 4
0xffe9e0 | 3
 | 0x40059b
main()
0xffe9d8
0x400546
%rsp
%rip
int main(int argc, char *argv[]) {
int i1 = 1;
int i2 = 2;
int i3 = 3;
int i4 = 4;
int result = func(&i1, &i2, &i3, &i4,
i1, i2, i3, i4);
…
}
int func(int *p1, int *p2, int *p3, int *p4,
int v1, int v2, int v3, int v4) {
…
}
0x40058c <+61>: lea 0x18(%rsp),%rsi
0x400591 <+66>: lea 0x1c(%rsp),%rdi
0x400596 <+71>: callq 0x400546 <func>
0x40059b <+76>: add $0x10,%rsp
…
2
%r9d
1
%r8d
0xffe9f0
%rcx
0xffe9f4
%rdx
0xffe9fc
%rdi
0xffe9f8
%rsi

## Slide 48: Register Restrictions
There is only one copy of registers for all programs and functions.
Problem: what if funcA is building up a value in register %r10, and calls funcB in the middle, which itself has instructions that modify %r10? funcA’s value will be destroyed!
Solution: lay down some "rules of the road" that callers and callees must follow when using registers so they do not interfere with one another.
These rules define two types of registers: caller-owned and callee-owned

## Slide 49: Caller/Callee
main
function1
function2
Caller/callee is terminology that refers to a pair of functions. A single function may be both a caller and callee simultaneously (e.g. function1 at right).
calls
calls
main is the caller, and function1 is the callee.
function1 is the caller, and function2 is the callee.

## Slide 50: Register Restrictions
Callee must save the existing value and restore it when done.
Caller can store values in them and assume they’ll be preserved across function calls.
Callee does not need to save the existing value.
Caller’s values could be overwritten by a callee! The caller may consider saving values elsewhere before calling functions.
Caller-Owned
Callee-Owned

## Slide 51: Caller-Owned Registers
main
function1
calls
main can use caller-owned registers and know that function1 will not permanently modify their values.
If function1 wants to use any caller-owned registers, it must save the existing values and restore them before returning.

## Slide 52: Caller-Owned Registers
function1:
push %rbp
push %rbx
...
pop %rbx
pop %rbp
retq
main
function1
calls

## Slide 53: Callee-Owned Registers
main can use callee-owned registers but calling function1 may permanently modify their values.
If function1 wants to use any callee-owned registers, it can do so without saving the existing values.
main
function1
calls

## Slide 54: Callee-Owned Registers
main
function1
calls
main:
...
push %r10
push %r11
callq function1
pop %r11
pop %r10
...

## Slide 55: A Day In the Life of function1
main
function1
function2
calls
calls
Caller-owned registers:
function1 must save/restore existing values of any it wants to use.
function1 can assume that calling function2 will not permanently change their values.
Callee-owned registers:
function1 does not need to save/restore existing values of any it wants to use.
calling function2 may permanently change their values.

## Slide 56: Example: Recursion
Let’s look at an example of recursion at the assembly level.
We’ll use everything we’ve learned about registers, the stack, function calls, parameters, and assembly instructions!
We’ll also see how helpful GDB can be when tracing through assembly.
rfact.c and rfact

## Slide 57: Our First Assembly
int sum_array(int arr[], int nelems) {
int sum = 0;
for (int i = 0; i < nelems; i++) {
sum += arr[i];
}
return sum;
}
0000000000401136 <sum_array>:
401136 <+0>: mov $0x0,%eax
40113b <+5>: mov $0x0,%edx
401140 <+10>: cmp %esi,%eax
401142 <+12>: jge 0x40114f <sum_array+25>
401144 <+14>: movslq %eax,%rcx
401147 <+17>: add (%rdi,%rcx,4),%edx
40114a <+20>: add $0x1,%eax
40114d <+23>: jmp 0x401140 <sum_array+10>
40114f <+25>: mov %edx,%eax
401151 <+27>: retq
We’re done with all our assembly lectures! Now we can fully understand what’s going on in the assembly below, including how someone would call sum_array in assembly and what the ret instruction does.