## Slide 1: CS107, Lecture 17 Assembly: Arithmetic and Logic Wrap, Control Flow
Reading: B&O 3.5-3.6
Ed Discussion

## Slide 2: Large Multiplication
Multiplying 64-bit numbers can produce a 128-bit result. How does x86-64 support this with only 64-bit registers?
If you specify two operands to imul, it multiplies them together and truncates it to fit in the second of the two 64-bit register operands.
imul S, D D ← D * S
If you specify one operand, it multiplies that by %rax and splits the product across 2 registers. It puts the high-order 64 bits in %rdx and the low-order 64 bits in %rax.
Instruction | Effect | Description
imulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Signed full multiply
mulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Unsigned full multiply

## Slide 3: Division and Remainder
Terminology: dividend / divisor = quotient with remainder
x86-64 supports dividing up to a 128-bit value by a 64-bit value.
The high-order 64 bits of the dividend need to be prepared and stored in %rdx, the low-order 64 bits in %rax. The divisor is the only listed operand.
The quotient is stored in %rax, and the remainder in %rdx.
Instruction | Effect | Description
idivq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Signed divide
divq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Unsigned divide

## Slide 4: Division and Remainder
Terminology: dividend / divisor = quotient with remainder
The high-order 64 bits of the dividend need to be prepared and stored in %rdx, the low-order 64 bits in %rax. The divisor is the only listed operand.
Most division uses only 64-bit dividends. The cqto instruction sign-extends the 64-bit value in %rax into %rdx to fill both registers with the dividend, as the division instruction expects.
Instruction | Effect | Description
idivq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Signed divide
divq S | R[%rdx] ← R[%rdx]:R[%rax] mod S; R[%rax] ← R[%rdx]:R[%rax] ➗ S | Unsigned divide
cqto | R[%rdx]:R[%rax] ← SignExtend(R[%rax]) | Convert to oct word

## Slide 5: Compiler Explorer Demo
https://godbolt.org/z/4cT75M4nd

## Slide 6: Code Reference: full_divide
// Returns x/y, stores remainder in location stored in remainder_ptr
long full_divide(long x, long y, long *remainder_ptr) {
long quotient = x / y;
long remainder = x % y;
*remainder_ptr = remainder;
return quotient;
}
-------
full_divide:
movq %rdi, %rax
movq %rdx, %rcx
cqto
idivq %rsi
movq %rdx, (%rcx)
ret

## Slide 7: Assembly Exercise 1
000000000040116e <sum_example1>:
40116e: 8d 04 37 lea (%rdi,%rsi,1),%eax
401171: c3 retq
Which of the following is most likely to have generated the above assembly?
// A) void sum_example1() { int x; int y; int sum = x + y; } | // B) int sum_example1(int x, int y) { return x + y; }
// C) void sum_example1(int x, int y) { int sum = x + y; } | 
Notes: Looks like we’re adding two uninitialized variables. BUT, remember register special uses!
B

## Slide 8: Assembly Exercise 2
0000000000401172 <sum_example2>:
401172: 8b 47 0c mov 0xc(%rdi),%eax
401175: 03 07 add (%rdi),%eax
401177: 2b 47 18 sub 0x18(%rdi),%eax
40117a: c3 retq
int sum_example2(int arr[]) { int sum = 0; sum += arr[0]; sum += arr[3]; sum -= arr[6]; return sum; } | What location or value in the assembly above represents the C code’s sum variable?
%eax
Notes: %eax

## Slide 9: Assembly Exercise 3
0000000000401172 <sum_example2>:
401172: 8b 47 0c mov 0xc(%rdi),%eax
401175: 03 07 add (%rdi),%eax
401177: 2b 47 18 sub 0x18(%rdi),%eax
40117a: c3 retq
int sum_example2(int arr[]) { int sum = 0; sum += arr[0]; sum += arr[3]; sum -= arr[6]; return sum; } | What location or value in the assembly code above represents the C code’s 6 (as in arr[6])?
0x18

## Slide 10: Reverse Engineering 1
int add_to(int x, int arr[], int i) {
int sum = ___?___;
sum += arr[___?___];
return ___?___;
}
----------
// x in %edi, arr in %rsi, i in %edx add_to:
movslq %edx, %rdx
movl %edi, %eax
addl (%rsi,%rdx,4), %eax
ret

## Slide 11: Reverse Engineering 1
int add_to(int x, int arr[], int i) {
int sum = ___?___;
sum += arr[___?___];
return ___?___;
}
----------
// x in %edi, arr in %rsi, i in %edx add_to:
movslq %edx, %rdx // sign-extend i into full register
movl %edi, %eax // copy x into %eax
addl (%rsi,%rdx,4), %eax // add arr[i] to %eax
ret

## Slide 12: Reverse Engineering 1
int add_to(int x, int arr[], int i) {
int sum = x;
sum += arr[i];
return sum;
}
----------
// x in %edi, arr in %rsi, i in %edx add_to:
movslq %edx, %rdx // sign-extend i into full register
movl %edi, %eax // copy x into %eax
addl (%rsi,%rdx,4), %eax // add arr[i] to %eax
ret

## Slide 13: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) {
int z = nums[___?___] * ___?___;
z -= ___?___;
z >>= ___?___;
return ___?___;
}
----------
// nums in %rdi, y in %esi elem_arithmetic:
movl %esi, %eax
imull (%rdi), %eax
subl 4(%rdi), %eax
sarl $2, %eax
addl $2, %eax
ret

## Slide 14: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) {
int z = nums[___?___] * ___?___;
z -= ___?___;
z >>= ___?___;
return ___?___;
}
----------
// nums in %rdi, y in %esi elem_arithmetic:
movl %esi, %eax // copy y into %eax
imull (%rdi), %eax // multiply %eax by nums[0]
subl 4(%rdi), %eax // subtract nums[1] from %eax
sarl $2, %eax // shift %eax right by 2
addl $2, %eax // add 2 to %eax
ret

## Slide 15: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) {
int z = nums[0] * y;
z -= nums[1];
z >>= 2;
return z + 2;
}
----------
// nums in %rdi, y in %esi elem_arithmetic:
movl %esi, %eax // copy y into %eax
imull (%rdi), %eax // multiply %eax by nums[0]
subl 4(%rdi), %eax // subtract nums[1] from %eax
sarl $2, %eax // shift %eax right by 2
addl $2, %eax // add 2 to %eax
ret

## Slide 16: Our First Assembly
int sum_array(int arr[], int nelems) {
int sum = 0;
for (int i = 0; i < nelems; i++) {
sum += arr[i];
}
return sum;
}
0000000000401136 <sum_array>:
401136: b8 00 00 00 00 mov $0x0,%eax
40113b: ba 00 00 00 00 mov $0x0,%edx
401140: 39 f0 cmp %esi,%eax
401142: 7d 0b jge 40114f <sum_array+0x19>
401144: 48 63 c8 movslq %eax,%rcx
401147: 03 14 8f add (%rdi,%rcx,4),%edx
40114a: 83 c0 01 add $0x1,%eax
40114d: eb f1 jmp 401140 <sum_array+0xa>
40114f: 89 d0 mov %edx,%eax
401151: c3 retq
We’re 1/2 of the way to understanding assembly! What looks understandable right now?

## Slide 17: Executing Instructions
What does it mean for a program to execute?

## Slide 18: Executing Instructions
So far:
Program values can be stored in memory or registers.
Assembly instructions read/write values back and forth between registers and main memory.
Assembly instructions are also stored in memory.
Today:
Who controls the instructions? How do we know what to do now or next?
Answer:
The program counter, stored in %rip.
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55

## Slide 19: Register Responsibilities
Some registers take on special responsibilities during program execution.
%rax stores the return value
%rdi stores the first parameter to a function
%rsi stores the second parameter to a function
%rdx stores the third parameter to a function
%rip stores the address of the next instruction to execute
%rsp stores the address of the current top of the stack
See the x86-64 Guide and Reference Sheet on the Resources webpage for more!

## Slide 20: Instructions Are Just Bytes!
0x0
Heap
Stack
Data
Text (code)
Machine code instructions
Main Memory

## Slide 21: %rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Heap
Stack
Data
Text (code)
Main Memory

## Slide 22: %rip
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Heap
Stack
Data
Text (code)
Main Memory
0x4004ed
%rip
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.

## Slide 23: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004ee
%rip
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 24: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f1
%rip
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 25: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004f8
%rip
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 26: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 27: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
Special hardware sets the program counter to the next instruction:
%rip += size of bytes of current instruction
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 28: Going In Circles
How can we use this representation of execution to represent e.g., a loop?
Key Idea: we can override what %rip stores and populate it with the address of an earlier instruction.

## Slide 29: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 30: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 31: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 32: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 33: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004fc
%rip
This assembly represents an infinite loop in C!
while (true) {…}
00000000004004ed <loop>:
4004ed: 55 push %rbp
4004ee: 48 89 e5 mov %rsp,%rbp
4004f1: c7 45 fc 00 00 00 00 movl $0x0,-0x4(%rbp)
4004f8: 83 45 fc 01 addl $0x1,-0x4(%rbp)
4004fc: eb fa jmp 4004f8 <loop+0xb>

## Slide 34: jmp
The jmp instruction jumps to another instruction in the assembly code (an "unconditional jump").
jmp Label (Direct Jump)
jmp *Operand (Indirect Jump)
The destination can be hardcoded into the instruction (direct jump):
jmp 404f8 <loop+0xb> # jump to instruction at 0x404f8
The destination can also be one of the usual operand forms (indirect jump):
jmp *%rax # jump to instruction at address in %rax

## Slide 35: "Interfering" with %rip
How do we repeat instructions in a loop?
jmp [target]
A 1-step unconditional jump (always jump when we execute this instruction)
What if we want a conditional jump?