## Slide 1: EE360: Lecture 10 Outline Capacity and Optimization of Ad Hoc Nets
Announcements
  Revised proposals due Monday
  HW 1 posted, due Feb. 19
  Lecture Wed will start at 9:15 (15 min early)
Definition of ad hoc network capacity
Capacity regions
Scaling laws and extensions
Achievable rate regions
Cross layer design
Network Utility Maximization

## Slide 2: Ad-Hoc Network Capacity
Fundamental limits on the maximum possible rates between all possible node pairs with vanishing probability of error
Independent of transmission and reception strategies (modulation, coding, routing, etc.)
Dependent on propagation, node capabilities (e.g. MIMO), transmit power, noise, etc
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 3: Network Capacity: What is it?
n(n-1)-dimensional region
  Rates between all node pairs
  Upper/lower bounds
    Lower bounds achievable
    Upper bounds hard
Other possible axes
  Energy and delay
R12
R34
Upper Bound
Lower Bound
Capacity
Delay
Energy
Upper Bound
Lower Bound
TX1
TX3
RX2
RX4

## Slide 4: Fundamental Network Capacity The Shangri-La of Information Theory
Much progress in finding the capacity limits of wireless single and multiuser channels
Limited understanding about the capacity limits of wireless networks, even for simple models
System assumptions such as constrained energy and delay may require new capacity definitions
Is this elusive goal the right thing to pursue?
Shangri-La is synonymous with any earthly paradise;
a permanently happy land, isolated from the outside world

## Slide 5: Some capacity questions
How to parameterize the region
  Power/bandwidth
  Channel models and CSI
  Outage probability
  Security/robustness
Defining capacity in terms of asymptotically small error and infinite delay has been highly enabling
  Has also been limiting
    Cause of unconsummated union in networks and IT
  What is the alternative?

## Slide 6: Network Capacity Results
Multiple access channel (MAC)
Broadcast channel
Relay channel upper/lower bounds
Strong interference channel
Scaling laws
Achievable rates for small networks
Gallager
Cover & Bergmans
Cover &
El Gamal
Gupta & Kumar
Sato, Han &
Kobayashi

## Slide 7: Capacity for Large Networks (Gupta/Kumar’00)
Make some simplifications and ask for less
  Each node has only a single destination
  All n nodes create traffic for their desired destination at a uniform rate l
  Capacity (throughput) is maximum nl that can be supported by the network (1 dimensional)
Throughput of random networks
  Network topology/packet destinations random.
  Throughput nl is random: characterized by its distribution as a function of network size n.
Find scaling laws for C(n)=l as n .

## Slide 8: Network Models
Dense networks
  Area is fixed and the density of nodes increases.
  Interference limited.
Extended networks
  Density is fixed and the area increases.
  coverage limited.
  Power limitation come into play

## Slide 9: Dense Network Results (area of network fixed)
Power falls off as d-a.
Critical Assumption:
  Signals received from other nodes (except one) are regarded as noise.
Nearest-neighbor multihop scheme many retransmissions!
Scaling no better than l=1/√𝒏
  Per-node rate l goes to zero!
  Upper bound proved by Gupta/Kumar’00
  Achievability proved by Francescetti’07

## Slide 10: Scaling Law Extensions (Dense Networks)
Fixed network topologies (Gupta/Kumar’01)
  Similar throughput bounds as random networks
Mobility in the network (Grossglauser/Tse’01):
  Mobiles pass message to neighboring nodes, eventually neighbor gets close to destination and forwards message
  Per-node throughput constant, aggregate throughput of order n, delay of order n.
  Chris’s presentation
Throughput/delay tradeoffs
  Piecewise linear model for throughput-delay tradeoff (ElGamal et. al’04, Toumpis/Goldsmith’04)
  Finite delay requires throughput penalty.
Achievable rates with multiuser coding/decoding (GK’03)
  Per-node throughput (bit-meters/sec) constant, aggregate infinite.
S
D

## Slide 11: Extended Networks
Xie and Kumar [3] addressed the question of scaling laws for the extended networks.
If a > 6, nearest neighbor multihopping is optimal.
  Many subsequent works relaxed the path loss condition down to a > 4 and obtained the same optimal scheme.
What about 2  a  4?
  Is nearest neighbor multihop scheme optimal?
  No!!!!
  Intuition: For a  4 the network is interference limited! Looks like a dense network.

## Slide 12: Hierarchical Cooperation in Large Networks (Ozgur et. al.)
Dense network model
Flat fading channels
  No multipath effects
  Line of sight type environment
The channel gains are known to all the nodes.
Far-Field Assumptions
Path loss and random phase.
Scaling is on the order of log n
  Per-node throughput increases with n!!!

## Slide 13: Achievable Scheme
Phase 1: local nodes form clusters, distribute bits within a cluster; concurrent transmissions
Phase 2: Virtual MIMO used to transmit bits between clusters: non-concurrent transmissions
Phase 3: Nodes quantize their received data and exchange within cluster; concurrent transmissions

## Slide 14: Ad Hoc Network Achievable Rate Regions
All achievable rate vectors between nodes
  Lower bounds Shannon capacity
An n(n-1) dimensional convex polyhedron
  Each dimension defines (net) rate from one node to each of the others
  Time-division strategy
  Link rates adapt to link SINR
  Optimal MAC via centralized scheduling
  Optimal routing
Yields performance bounds
  Evaluate existing protocols
  Develop new protocols
3
1
2
4
5

## Slide 15: Achievable Rates
A matrix R belongs to the capacity region if there are rate matrices R1, R2, R3 ,…, Rn such that
Linear programming problem:
  Need clever techniques to reduce complexity
  Power control, fading, etc., easily incorporated
  Region boundary achieved with optimal routing
Achievable rate
vectors achieved
by time division
Capacity region
is convex hull of
all rate matrices

## Slide 16: Example: Six Node Network
Capacity region is 30-dimensional

## Slide 17: Capacity Region Slice (6 Node Network)
(a): Single hop, no simultaneous
transmissions.
(b): Multihop, no simultaneous
transmissions.
(c): Multihop, simultaneous
transmissions.
(d): Adding power control
(e): Successive interference
cancellation, no power
control.
Multiple
hops
Spatial
reuse
SIC
Extensions:
- Capacity vs. network size
- Capacity vs. topology
- Fading and mobility
- Multihop cellular

## Slide 18: Is a capacity region all we need to design networks?
Yes, if the application and network design can be decoupled
Capacity
Delay
Energy
Application metric: f(C,D,E):
(C*,D*,E*)=arg max f(C,D,E)
(C*,D*,E*)
If application and network design are
coupled, then cross-layer design needed

## Slide 19: Crosslayer Design in Ad-Hoc Wireless Networks
Application
Network
Access
Link
Hardware
Substantial gains in throughput, efficiency, and end-to-end performance from cross-layer design
Notes: Interdisciplinary research, design, and development very challenging, but necessary to meet the requirements of future wireless applications

## Slide 20: Why a crosslayer design?
The technical challenges of future mobile networks cannot be met with a layered design approach.
QoS cannot be provided unless it is supported across all layers of the network.
  The application must adapt to the underlying channel and network characteristics.
  The network and link must adapt to the application requirements
Interactions across network layers must be understood and exploited.

## Slide 21: Delay/Throughput/Robustness across Multiple Layers
Multiple routes through the network can be used for multiplexing or reduced delay/loss
Application can use single-description or multiple description codes
Can optimize optimal operating point for these tradeoffs to minimize distortion
A
B

## Slide 22: Cross-layer protocol design for real-time media
Application layer
Network layer
MAC layer
Link layer
Capacity assignment for multiple service classes
Congestion-distortion optimized
routing
Adaptive
link layer techniques
Loss-resilient source coding and packetization
Congestion-distortion optimized
scheduling
Traffic flows
Link capacities
Link state information
Transport layer
Rate-distortion preamble
Joint with T. Yoo, E. Setton,
X. Zhu, and B. Girod

## Slide 23: Video streaming performance
3-fold increase
5 dB
100
s
(logarithmic scale)
1000

## Slide 24: Approaches to Cross-Layer Resource Allocation*
Network
Optimization
Dynamic
Programming
State Space
Reduction
*Much prior work is for wired/static networks
Distributed
Optimization
Distributed
Algorithms
Network Utility
Maximization
Wireless NUM
Multiperiod NUM
Game
Theory
Mechanism Design
Stackelberg Games
Nash Equilibrium

## Slide 25: Network Utility Maximization
Maximizes a network utility function
Assumes
  Steady state
  Reliable links
  Fixed link capacities
Dynamics are only in the queues
routing
Fixed link capacity
flow k
U1(r1)
U2(r2)
Un(rn)
Ri
Rj
Notes: 1 NUM views network protocols as optimization algorithms
2 Underlying problem is…
2.1 max the sum of the utilities
2.2 sum of the flows across a link cannot exceed the capacity of the link

## Slide 26: Wireless NUM
Extends NUM to random environments
Network operation as stochastic optimization algorithm
Physical
Layer
Upper
Layers
Physical
Layer
Upper
Layers
Physical
Layer
Upper
Layers
Physical
Layer
Upper
Layers
Physical
Layer
Upper
Layers
user
video
Stolyar, Neely, et. al.
Notes: The highlighted points are the keys
Dwell on rate/rel/delay tradeoffs

## Slide 27: WNUM Policies
Control network resources
Inputs:
  Random network channel information Gk
  Network parameters
  Other policies
Outputs:
  Control parameters
  Optimized performance, that
  Meet constraints
Channel sample driven policies
Notes: The policies are functions or algorithms
The inputs are channel state and other parameters set by the network operator
The lagrange multipliers are Markov

## Slide 28: Example: NUM and Adaptive Modulation
Policies
  Information rate
  Tx power
  Tx Rate
  Tx code rate
Policy adapts to
  Changing channel conditions
  Packet backlog
  Historical power usage
Data
Data
Data
Physical
Layer
Buffer
Upper
Layers
Physical
Layer
Buffer
Upper
Layers
Block codes used
Notes: Simplest model for illustration of concepts:
Multiple users over a single link
Each is buffered before going over the link
The link uses block codes at rate 0<code rate<1
System adjusts code rate, power, and tx rate to maximize user satisfaction

## Slide 29: Rate-Delay-Reliability
Policy Results
Notes: WNUM –with no codes used- offers superior performance.
The rate delay curve illustrates this best.

## Slide 30: Game theory
Coordinating user actions in a large ad-hoc network can be infeasible
Distributed control difficult to derive and computationally complex
Game theory provides a new paradigm
  Users act to “win” game or reach an equilibrium
  Users heterogeneous and non-cooperative
  Local competition can yield optimal outcomes
  Dynamics impact equilibrium and outcome
  Adaptation via game theory

## Slide 31: Limitations in theory of ad hoc networks today
  Shannon capacity pessimistic for wireless channels and intractable for large networks
Wireless
Information
Theory
Optimization
Theory
B. Hajek and A. Ephremides, “Information theory and communications
networks: An unconsummated union,” IEEE Trans. Inf. Theory, Oct. 1998.
  Little cross-disciplinary work spanning these fields
  Optimization techniques applied to given network models, which rarely take into account fundamental network capacity or dynamics
Wireless
Network
Theory
  Large body of wireless (and wired) network theory that is ad-hoc, lacks a basis in fundamentals, and lacks an objective success criteria.
Notes: Control theory here is not blue, the success criteria is not blue since can’t solve problems that don’t fit the math

## Slide 32: Consummating Unions
When capacity is not the only metric, a new theory is needed to deal with nonasymptopia (i.e. delay, random traffic) and application requirements
  Shannon theory generally breaks down when delay, error, or user/traffic dynamics must be considered
Fundamental limits are needed outside asymptotic regimes
Optimization, game theory, and other techniques provide the missing link
Wireless
Information
Theory
Wireless
Network
Theory
Optimization
Game Theory,…
Menage a Trois
Notes: Bob’s comments:
Wireless information theory has attacked too many problems
Control and optimization has been too focused on the math, and not on problems that don’t fit the math.

## Slide 33: Summary
Capacity of wireless ad hoc networks largely unknown, even for simple canonical models.
Scaling laws, degrees of freedom (interference alignment) and other approximations promising
Capacity not the only metric of interest
Cross layer design requires new tools such as optimization and game theory
Consummating unions in ad-hoc networks a great topic of research

## Slide 34: Presentation
“Mobility Increases the Capacity of Ad-hoc Wireless Networks”
Authors: Grossglauser and Tse.
Appeared in IEEE INFOCOM 2001
  journal version in ACM/IEEE Trans. Networking
Presented by Chris