## Slide 1: CS107, Lecture 11 Assembly Continued
This document is copyright (C) Stanford Computer Science, Lisa Yan, and Nick Troccoli, licensed under Creative Commons Attribution 2.5 License. All rights reserved.
Based on slides created by Marty Stepp, Cynthia Lee, Chris Gregg, and others.
Reading: B&O 3.1-3.4

## Slide 2: Lecture Plan
7
Recap: mov so far
Data and Register Sizes
The lea Instruction
Logical and Arithmetic Operations
Practice: Reverse Engineering
1
11
24
30
38
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 3: mov
8
The mov instruction copies bytes from one place to another; it is similar to the assignment operator (=) in C.
mov src,dst
The src and dst can each be one of:
Immediate (constant value, like a number) (only src)
Register
Memory Location
(at most one of src, dst)

## Slide 4: Memory Location Syntax
Syntax | Meaning
0x104 | Address 0x104 (no $)
(%rax) | What’s in %rax
4(%rax) | What’s in %rax, plus 4
(%rax, %rdx) | Sum of what’s in %rax and %rdx
4(%rax, %rdx) | Sum of values in %rax and %rdx, plus 4
(, %rcx, 4) | What’s in %rcx, times 4 (multiplier can be 1, 2, 4, 8)
(%rax, %rcx, 2) | What’s in %rax, plus 2 times what’s in %rcx
8(%rax, %rcx, 2) | What’s in %rax, plus 2 times what’s in %rcx, plus 8 9

## Slide 5: Operand Forms
10
Type | Form | Operand Value |  | Name
Immediate | $𝐼𝑚𝑚 | 𝐼𝑚𝑚 |  | Immediate
Register | 𝑟! | R[𝑟!] |  | Register
Memory | 𝐼𝑚𝑚 | M[𝐼𝑚𝑚] |  | Absolute
Memory | (𝑟!) | M[R 𝑟! ] |  | Indirect
Memory | 𝐼𝑚𝑚(𝑟") | M[𝐼𝑚𝑚 + R 𝑟" ] |  | Base + displacement
Memory | (𝑟", 𝑟# ) | M[R 𝑟" + R 𝑟# ] |  | Indexed
Memory | 𝐼𝑚𝑚(𝑟", 𝑟# ) | M[𝐼𝑚𝑚 + R 𝑟" + R 𝑟# ] |  | Indexed
Memory | (, 𝑟# , 𝑠) | M[R 𝑟# . 𝑠] |  | Scaled indexed
Memory | 𝐼𝑚𝑚(, 𝑟# , 𝑠) | M[𝐼𝑚𝑚 + R 𝑟# . 𝑠] |  | Scaled indexed
Memory | (𝑟", 𝑟# , 𝑠) | M[R 𝑟" + R 𝑟# . 𝑠] |  | Scaled indexed
Memory | 𝐼𝑚𝑚(𝑟", 𝑟# , 𝑠) | M[𝐼𝑚𝑚 + R 𝑟" + R 𝑟# | . 𝑠] | Scaled indexed
Figure 3.3 from the book: “Operand forms. Operands can denote immediate (constant) values, register values, or values from memory. The scaling factor s must be either. 1, 2, 4, or 8.”

## Slide 6: Lecture Plan
11
Recap: mov so far
Data and Register Sizes
The lea Instruction
Logical and Arithmetic Operations
Practice: Reverse Engineering
1
11
24
30
38
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 7: Data Sizes
12
Data sizes in assembly have slightly different terminology to get used to:
A byte is 1 byte.
A word is 2 bytes.
A double word is 4 bytes.
A quad word is 8 bytes.
Assembly instructions can have suffixes to refer to these sizes:
b means byte
w means word
l means double word
q means quad word

## Slide 8: Register Sizes
63
Bit:
0
7
15
31
%rax | %eax | %ax | %al
%rbx | %ebx | %bx | %bl
%rcx | %ecx | %cx | %cl
%rdx | %edx | %dx | %dl
%rsi | %esi | %si | %sil
%rdi | %edi | %di | %dil

## Slide 9: Register Sizes
63
Bit:
0
7
15
31
%rbp | %ebp | %bp | %bpl
%rsp | %esp | %sp | %spl
%r8 | %r8d | %r8w | %r8b
%r9 | %r9d | %r9w | %r9b
%r10 | %r10d | %r10w | %r10b
%r11 | %r11d | %r11w | %r11b

## Slide 10: Register Sizes
63
Bit:
0
7
15
31
%r12 | %r12d | %r12w | %r12b
%r13 | %r13d | %r13w | %r13b
%r14 | %r14d | %r14w | %r14b
%r15 | %r15d | %r15w | %r15b

## Slide 11: Register Responsibilities
16
Some registers take on special responsibilities during program execution.
%rax stores the return value
%rdi stores the first parameter to a function
%rsi stores the second parameter to a function
%rdx stores the third parameter to a function
%rip stores the address of the next instruction to execute
%rsp stores the address of the current top of the stack
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 12: mov Variants
mov can take an optional suffix (b,w,l,q) that specifies the size of data to move:
movb, movw, movl, movq
mov only updates the specific register bytes or memory locations indicated.
  Exception: movl writing to a register will also set high order 4 bytes to 0.

## Slide 13: Practice: mov And Data Sizes
For each of the following mov instructions, determine the appropriate suffix based on the operands (e.g. movb, movw, movl or movq).
mov %eax, (%rsp)
mov (%rax), %dx
mov $0xff, %bl
mov (%rsp,%rdx,4),%dl
mov (%rdx), %rax
mov %dx, (%rax)

## Slide 14: Practice: mov And Data Sizes
For each of the following mov instructions, determine the appropriate suffix based on the operands (e.g. movb, movw, movl or movq).
movl %eax, (%rsp)
movw (%rax), %dx
movb $0xff, %bl
movb (%rsp,%rdx,4),%dl
movq (%rdx), %rax
movw %dx, (%rax)

## Slide 15: mov
The movabsq instruction is used to write a 64-bit Immediate (constant) value.
The regular movq instruction can only take 32-bit immediates.
64-bit immediate as source, only register as destination.
movabsq $0x0011223344556677, %rax

## Slide 16: movz and movs
There are two mov instructions that can be used to copy a smaller source to a larger destination: movz and movs.
movz fills the remaining bytes with zeros
movs fills the remaining bytes by sign-extending the most significant bit in the source.
The source must be from memory or a register, and the destination is a register.

## Slide 17: movz and movs
Instruction | Description
movzbw | Move zero-extended byte to word
movzbl | Move zero-extended byte to double word
movzwl | Move zero-extended word to double word
movzbq | Move zero-extended byte to quad word
movzwq | Move zero-extended word to quad word
MOVZ S,R
R ← ZeroExtend(S)

## Slide 18: movz and movs
Instruction | Description
movsbw | Move sign-extended byte to word
movsbl | Move sign-extended byte to double word
movswl | Move sign-extended word to double word
movsbq | Move sign-extended byte to quad word
movswq | Move sign-extended word to quad word
movslq | Move sign-extended double word to quad word
cltq | Sign-extend %eax to %rax %rax <- SignExtend(%eax)
MOVS S,R
R ← SignExtend(S)

## Slide 19: Lecture Plan
24
Recap: mov so far
Data and Register Sizes
The lea Instruction
Logical and Arithmetic Operations
Practice: Reverse Engineering
7
11
24
30
38
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 20: lea
The lea instruction copies an “effective address” from one place to another.
lea src,dst
Unlike mov, which copies data at the address src to the destination, lea copies the value of src itself to the destination.
The syntax for the destinations is the same as
mov. The difference is how it handles the src.

## Slide 21: lea vs. mov
Operands | mov Interpretation | lea Interpretation
6(%rax), %rdx | Go to the address (6 + what’s in %rax), and copy data there into %rdx | Copy 6 + what’s in %rax into %rdx.

## Slide 22: lea vs. mov
Operands | mov Interpretation | lea Interpretation
6(%rax), %rdx | Go to the address (6 + what’s in %rax), and copy data there into %rdx | Copy 6 + what’s in %rax into %rdx.
(%rax, %rcx), %rdx | Go to the address (what’s in %rax + what’s in %rcx) and copy data there into %rdx | Copy (what’s in %rax + what’s in %rcx) into %rdx.

## Slide 23: lea vs. mov
Operands | mov Interpretation | lea Interpretation
6(%rax), %rdx | Go to the address (6 + what’s in %rax), and copy data there into %rdx | Copy 6 + what’s in %rax into %rdx.
(%rax, %rcx), %rdx | Go to the address (what’s in %rax + what’s in %rcx) and copy data there into %rdx | Copy (what’s in %rax + what’s in %rcx) into %rdx.
(%rax, %rcx, 4), %rdx | Go to the address (%rax + 4 * %rcx) and copy data there into %rdx. | Copy (%rax + 4 * %rcx) into %rdx.

## Slide 24: lea vs. mov
Operands | mov Interpretation | lea Interpretation
6(%rax), %rdx | Go to the address (6 + what’s in %rax), and copy data there into %rdx | Copy 6 + what’s in %rax into %rdx.
(%rax, %rcx), %rdx | Go to the address (what’s in %rax + what’s in %rcx) and copy data there into %rdx | Copy (what’s in %rax + what’s in %rcx) into %rdx.
(%rax, %rcx, 4), %rdx | Go to the address (%rax + 4 * %rcx) and copy data there into %rdx. | Copy (%rax + 4 * %rcx) into %rdx.
7(%rax, %rax, 8), %rdx | Go to the address (7 + %rax + 8 * %rax) and copy data there into %rdx. | Copy (7 + %rax + 8 * %rax) into %rdx.
Unlike mov, which copies data at the address src to the destination, lea copies the value of src itself to the destination.

## Slide 25: Lecture Plan
30
Recap: mov so far
Data and Register Sizes
The lea Instruction
Logical and Arithmetic Operations
Practice: Reverse Engineering
7
11
24
30
38
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 26: Unary Instructions
31
The following instructions operate on a single operand (register or memory):
Examples:
incq 16(%rax) dec %rdx
not %rcx
Instruction Effect Description |  |  |  |  | 
inc | D | D | ← | D + 1 | Increment
dec | D | D | ← | D - 1 | Decrement
neg | D | D | ← | -D | Negate
not | D | D | ← | ~D | Complement

## Slide 27: Binary Instructions
32
The following instructions operate on two operands (both can be register or memory, source can also be immediate). Both cannot be memory locations. Read it as, e.g. “Subtract S from D”:
Examples:
addq %rcx,(%rax)
xorq $16,(%rax, %rdx, 8) subq %rdx,8(%rax)
Instruction Effect Description |  |  |  |  | 
add S, D | D | ← | D + | S | Add
sub S, D | D | ← | D - | S | Subtract
imul S, D | D | ← | D * | S | Multiply
xor S, D | D | ← | D ^ | S | Exclusive-or
or S, D | D | ← | D ¦ | S | Or
and S, D | D | ← | D & | S | And

## Slide 28: Large Multiplication
Multiplying 64-bit numbers can produce a 128-bit result. How does x86-64 support this with only 64-bit registers?
If you specify two operands to imul, it multiplies them together and truncates until it fits in a 64-bit register.
imul S, D D ← D * S
If you specify one operand, it multiplies that by %rax, and splits the product across 2 registers. It puts the high-order 64 bits in %rdx and the low-order 64 bits in %rax.
Instruction | Effect | Description
imulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Signed full multiply
mulq S | R[%rdx]:R[%rax] ← S x R[%rax] | Unsigned full multiply

## Slide 29: Division and Remainder
Terminology: dividend / divisor = quotient + remainder
x86-64 supports dividing up to a 128-bit value by a 64-bit value.
The high-order 64 bits of the dividend are in %rdx, and the low-order 64 bits are in %rax. The divisor is the operand to the instruction.
The quotient is stored in %rax, and the remainder in %rdx.
Instruction | Effect |  |  |  | Description
idivq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Signed divide
divq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Unsigned divide

## Slide 30: Division and Remainder
Terminology: dividend / divisor = quotient + remainder
The high-order 64 bits of the dividend are in %rdx, and the low-order 64 bits are in %rax. The divisor is the operand to the instruction.
Most division uses only 64-bit dividends. The cqto instruction sign-extends the 64-bit value in %rax into %rdx to fill both registers with the dividend, as the division instruction expects.
Instruction | Effect |  |  |  | Description
idivq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Signed divide
divq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Unsigned divide
cqto | R[%rdx]:R[%rax] ← SignExtend(R[%rax]) |  |  |  | Convert to oct word

## Slide 31: Shift Instructions
The following instructions have two operands: the shift amount k and the destination to shift, D. k can be either an immediate value, or the byte register
%cl (and only that register!)
Examples:
shll $3,(%rax)
shrl %cl,(%rax,%rdx,8) sarl $4,8(%rax)
Instruction Effect Description |  |  |  |  |  | 
sal | k, D | D | ← | D | << k | Left shift
shl | k, D | D | ← | D | << k | Left shift (same as sal)
sar | k, D | D | ← | D | >>A k | Arithmetic right shift
shr | k, D | D | ← | D | >>L k | Logical right shift

## Slide 32: Shift Amount
When using %cl, the width of what you are shifting determines what portion of %cl is used.
For w bits of data, it looks at the low-order log2(w) bits of %cl to know how much to shift.
  If %cl = 0xff, then: shlb shifts by 7 because it considers only the low-order log2(8) = 3 bits, which represent 7. shlw shifts by 15 because it considers only the low-order log2(16) = 4 bits, which represent 15.
Instruction Effect Description |  |  |  |  |  | 
sal | k, D | D | ← | D | << k | Left shift
shl | k, D | D | ← | D | << k | Left shift (same as sal)
sar | k, D | D | ← | D | >>A k | Arithmetic right shift
shr | k, D | D | ← | D | >>L k | Logical right shift

## Slide 33: Lecture Plan
38
Recap: mov so far
Data and Register Sizes
The lea Instruction
Logical and Arithmetic Operations
Practice: Reverse Engineering
7
11
24
30
38
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 34: Assembly Exploration
Let’s pull these commands together and see how some C code might be translated to assembly.
Compiler Explorer is a handy website that lets you quickly write C code and see its assembly translation. Let’s check it out!
https://godbolt.org/z/WPzz6G4a9

## Slide 35: Executing Instructions: JUMP!
What does it mean for a program to execute?

## Slide 36: Executing Instructions
So far:
Program values can be stored in memory or registers.
Assembly instructions read/write values back and forth between registers (on the CPU) and memory.
Assembly instructions are also stored in memory.
So now:
Who controls the instructions?
How do we know what to do now or next?
Answer:
The program counter (PC), %rip.
4004fd 4004fc
4004fb 4004fa 4004f9
4004f8
4004f7
4004f6
4004f5
4004f4
4004f3
4004f2
4004f1
4004f0
4004ef 4004ee 4004ed
fa
eb
01
fc
45
83
00
00
00
00
fc
45
c7
e5
89
48
55

## Slide 37: Register Responsibilities
Some registers take on special responsibilities during program execution.
%rax stores the return value
%rdi stores the first parameter to a function
%rsi stores the second parameter to a function
%rdx stores the third parameter to a function
%rip stores the address of the next instruction to execute
%rsp stores the address of the current top of the stack
See the x86-64 Guide and Reference Sheet on the Resources webpage for more!

## Slide 38: Instructions Are Just Bytes!

## Slide 39: Instructions Are Just Bytes!

## Slide 40: Instructions Are Just Bytes!
0x0
Stack
Heap
Data
Text (code)
Machine code instructions
Main Memory

## Slide 41: %rip 4004fd
p
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: 4004fc: | 83 eb | 45 fa | fc | 01 |  |  |  | addl jmp | $0x1,-0x4(%rbp) 4004f8 <loop+0xb>
 | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Stack
Heap
Data
Text (code)
Main Memory

## Slide 42: %rip
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004ed
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
%rip

## Slide 43: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
0x4004ee
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>
%rip

## Slide 44: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
0x4004f1
%rip
15
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 45: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
0x4004f8
%rip
16
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 46: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
The program counter (PC), known as %rip in x86-64, stores the address in memory of the next instruction to be executed.
0x4004fc
%rip
17
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 47: %rip
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
Special hardware sets the program counter to the next instruction:
%rip += size of bytes of current instruction
0x4004fc
%rip
18
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 48: Going In Circles
19
How can we use this representation of execution to represent e.g. a loop?
Key Idea: we can ”interfere” with %rip and set it back to an earlier instruction!

## Slide 49: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
0x4004fc
%rip
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 50: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
0x4004fc
%rip

## Slide 51: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
0x4004fc
%rip
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>

## Slide 52: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>
The jmp instruction is an unconditional jump that sets the program counter to the jump target (the operand).
0x4004fc
%rip

## Slide 53: Jump!
4004fd | fa
4004fc | eb
4004fb | 01
4004fa | fc
4004f9 | 45
4004f8 | 83
4004f7 | 00
4004f6 | 00
4004f5 | 00
4004f4 | 00
4004f3 | fc
4004f2 | 45
4004f1 | c7
4004f0 | e5
4004ef | 89
4004ee | 48
4004ed | 55
This assembly represents an infinite loop in C!
00000000004004ed <loop>:
4004ed: | 55 |  |  |  |  |  |  | push | %rbp
4004ee: | 48 | 89 | e5 |  |  |  |  | mov | %rsp,%rbp
4004f1: | c7 | 45 | fc | 00 | 00 | 00 | 00 | movl | $0x0,-0x4(%rbp)
4004f8: | 83 | 45 | fc | 01 |  |  |  | addl | $0x1,-0x4(%rbp)
4004fc: | eb | fa |  |  |  |  |  | jmp | 4004f8 <loop+0xb>
0x4004fc
while
(true)
{…}
%rip

## Slide 54: jmp
The jmp instruction jumps to another instruction in the assembly code (“Unconditional Jump”).
jmp Label jmp *Operand
(Direct Jump) (Indirect Jump)
The destination can be hardcoded into the instruction (direct jump):
jmp 404f8 <loop+0xb> # jump to instruction at 0x404f8
The destination can also be one of the usual operand forms (indirect jump):
jmp *%rax # jump to instruction at address in %rax

## Slide 55: “Interfering” with %rip
How do we repeat instructions in a loop?
jmp [target]
  A 1-step unconditional jump (always jump when we execute this instruction)
What if we want a conditional jump?

## Slide 56
We’ll leave that for next time….

## Slide 57: Code Reference: add_to_first
// Returns the sum of x and the first element in arr
int add_to_first(int x, int arr[]) {
int sum = x; sum += arr[0]; return sum;
}
add_to_first: movl %edi, %eax
addl (%rsi), %eax
ret

## Slide 58: Code Reference: full_divide
// Returns x/y, stores remainder in location stored in remainder_ptr
long full_divide(long x, long y, long *remainder_ptr) {
long quotient = x / y;
long remainder = x % y;
*remainder_ptr = remainder;
return quotient;
}
full_divide:
41
ret
movq | %rdi, | %rax
movq | %rdx, | %rcx
cqto |  | 
idivq | %rsi | 
movq | %rdx, | (%rcx)

## Slide 59: Assembly Exercise 1
42
000000000040116e <sum_example1>:
40116e: 8d 04 37
401171: c3
lea (%rdi,%rsi,1),%eax retq
Which of the following is most likely to have generated the above assembly?
// A)
void sum_example1() { int x;
int y;
int sum = x + y;
}
// C)
void sum_example1(int x, int y) { int sum = x + y;
}
// B)
int sum_example1(int x, int y) { return x + y;
}

## Slide 60: Assembly Exercise 2
0000000000401172 <sum_example2>:
401172: | 8b | 47 | 0c | mov | 0xc(%rdi),%eax
401175: | 03 | 07 |  | add | (%rdi),%eax
401177: 40117a: | 2b c3 | 47 | 18 | sub retq | 0x18(%rdi),%eax
int sum_example2(int arr[]) { int sum = 0;
sum += arr[0];
sum += arr[3]; sum -= arr[6];
return sum;
}
What location or value in the assembly above represents the C code’s sum variable?

## Slide 61: Assembly Exercise 3
0000000000401172 <sum_example2>:
401172: | 8b | 47 | 0c | mov | 0xc(%rdi),%eax
401175: | 03 | 07 |  | add | (%rdi),%eax
401177: 40117a: | 2b c3 | 47 | 18 | sub retq | 0x18(%rdi),%eax
int sum_example2(int arr[]) { int sum = 0;
sum += arr[0];
sum += arr[3]; sum -= arr[6];
return sum;
}
What location or value in the assembly code above represents the C code’s 6 (as in arr[6])?

## Slide 62: Our First Assembly
45
int sum_array(int arr[], int nelems) { int sum = 0;
for (int i = 0; i < nelems; i++) { sum += arr[i];
}
return sum;
}
0000000000401136 <sum_array>:
401136: | b8 | 00 | 00 | 00 | 00 | mov | $0x0,%eax
40113b: 401140: | ba 39 | 00 f0 | 00 | 00 | 00 | mov cmp | $0x0,%edx %esi,%eax
401142: | 7d | 0b |  |  |  | jge | 40114f <sum_array+0x19>
401144: | 48 | 63 | c8 |  |  | movslq | %eax,%rcx
401147: | 03 | 14 | 8f |  |  | add | (%rdi,%rcx,4),%edx
40114a: 40114d: | 83 eb | c0 f1 | 01 |  |  | add jmp | $0x1,%eax 401140 <sum_array+0xa>
40114f: | 89 | d0 |  |  |  | mov | %edx,%eax
401151: | c3 |  |  |  |  | retq | 
We’re 1/2 of the way to understanding assembly!
What looks understandable right now?

## Slide 63: A Note About Operand Forms
Many instructions share the same address operand forms that mov uses.
  Eg. 7(%rax, %rcx, 2).
These forms work the same way for other instructions, e.g. sub:
  sub 8(%rax,%rdx),%rcx -> Go to 8 + %rax + %rdx, subtract what’s there from %rcx
The exception is lea:
  It interprets this form as just the calculation, not the dereferencing
  lea 8(%rax,%rdx),%rcx -> Calculate 8 + %rax + %rdx, put it in %rcx

## Slide 64: Shift Amount
When using %cl, the width of what you are shifting determines what portion of %cl is used.
For w bits of data, it looks at the low-order log2(w) bits of %cl to know how much to shift.
  If %cl = 0xff, then: shlb shifts by 7 because it considers only the low-order log2(8) = 3 bits, which represent 7. shlw shifts by 15 because it considers only the low-order log2(16) = 4 bits, which represent 15.
Instruction Effect Description |  |  |  |  |  | 
sal | k, D | D | ← | D | << k | Left shift
shl | k, D | D | ← | D | << k | Left shift (same as sal)
sar | k, D | D | ← | D | >>A k | Arithmetic right shift
shr | k, D | D | ← | D | >>L k | Logical right shift

## Slide 65: Division and Remainder
Terminology: dividend / divisor = quotient + remainder
x86-64 supports dividing up to a 128-bit value by a 64-bit value.
The high-order 64 bits of the dividend are in %rdx, and the low-order 64 bits are in %rax. The divisor is the operand to the instruction.
The quotient is stored in %rax, and the remainder in %rdx.
Instruction | Effect |  |  |  | Description
idivq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Signed divide
divq S | R[%rdx] R[%rax] | ← ← | R[%rdx]:R[%rax] R[%rdx]:R[%rax] | mod S; S | Unsigned divide

## Slide 66: Extra Practice
https://godbolt.org/z/hGKPWszq4

## Slide 67: Reverse Engineering 1
int add_to(int x, int arr[], int i) { int sum = ? ;
sum += arr[ ? ];
return ? ;
}
add_to:
movslq %edx, %rdx movl %edi, %eax
addl (%rsi,%rdx,4), %eax ret

## Slide 68: Reverse Engineering 1
int add_to(int x, int arr[], int i) { int sum = ? ;
sum += arr[ ? ];
return ? ;
}
// x in %edi, arr in %rsi, i in %edx add_to:
// sign-extend i into full register
// copy x into %eax
// add arr[i] to %eax
movslq %edx, %rdx movl %edi, %eax
addl (%rsi,%rdx,4), %eax ret

## Slide 69: Reverse Engineering 1
int add_to(int x, int arr[], int i) { int sum = x;
sum += arr[i];
return sum;
}
// x in %edi, arr in %rsi, i in %edx add_to:
// sign-extend i into full register
// copy x into %eax
// add arr[i] to %eax
movslq %edx, %rdx movl %edi, %eax
addl (%rsi,%rdx,4), %eax ret

## Slide 70: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) { int z = nums[ ? ] * ? ;
z -= ? ;
z >>= ? ; return ? ;
}
elem_arithmetic: movl %esi, %eax imull (%rdi), %eax subl 4(%rdi), %eax sarl $2, %eax addl $2, %eax
ret

## Slide 71: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) { int z = nums[ ? ] * ? ;
z -= ? ;
z >>= ? ; return ? ;
}
// nums in %rdi, y in %esi elem_arithmetic:
addl
ret
$2,
%eax
//
add
2
to
%eax
movl %esi, %eax imull (%rdi), %eax subl 4(%rdi), %eax sarl $2, %eax
// copy y into %eax
// multiply %eax by nums[0]
// subtract nums[1] from %eax
// shift %eax right by 2

## Slide 72: Reverse Engineering 2
int elem_arithmetic(int nums[], int y) { int z = nums[0] * y;
z -= nums[1];
z >>= 2;
return z + 2;
}
// nums in %rdi, y in %esi elem_arithmetic:
addl
ret
$2,
%eax
//
add
2
to
%eax
movl %esi, %eax imull (%rdi), %eax subl 4(%rdi), %eax sarl $2, %eax
// copy y into %eax
// multiply %eax by nums[0]
// subtract nums[1] from %eax
// shift %eax right by 2

## Slide 73: Reverse Engineering 3
long func(long x, long *ptr) {
*ptr = ? + 1;
long result = x % ? ; return ? ;
}
func:
movq %rdi, %rax leaq 1(%rdi), %rcx movq %rcx, (%rsi) cqto
idivq %rcx
movq
ret
%rdx,
%rax

## Slide 74: Reverse Engineering 3
long func(long x, long *ptr) {
*ptr = ? + 1;
long result = x % ? ; return ? ;
}
// x in %rdi, ptr in %rsi func:
movq %rdi, %rax leaq 1(%rdi), %rcx movq %rcx, (%rsi)
movq
ret
%rdx,
%rax
//
copy
the
remainder
into
%rax
// copy x into %rax
// put x + 1 into %rcx
// copy %rcx into *ptr
cqto |  | // | sign-extend | x | into | %rdx
idivq | %rcx | // | calculate x | / | (x + | 1)

## Slide 75: Reverse Engineering 3
long func(long x, long *ptr) {
*ptr = x + 1;
long result = x % *ptr; // or x + 1
return result;
}
// x in %rdi, ptr in %rsi func:
movq %rdi, %rax leaq 1(%rdi), %rcx movq %rcx, (%rsi)
movq
ret
%rdx,
%rax
//
copy
the
remainder
into
%rax
// copy x into %rax
// put x + 1 into %rcx
// copy %rcx into *ptr
cqto |  | // | sign-extend | x | into | %rdx
idivq | %rcx | // | calculate x | / | (x + | 1)

## Slide 76: Side Note: Old GCC Output
long func(long x, long *ptr) {
*ptr = x + 1;
long result = x % *ptr; // or x + 1
return result;
}
// x in %rdi, ptr in %rsi func:
leaq 1(%rdi), %rcx movq %rcx, (%rsi) movq %rdi, %rax
cqto idivq %rcx
movq
ret
%rdx,
%rax
//
copy
the
remainder
into
%rax
// put x + 1 into %rcx
// copy %rcx into *ptr
// copy x into %rax
// sign-extend x into %rdx
// calculate x / (x + 1)