## Slide 1: CS107, Lecture 19 Assembly: Control Flow and Function Calls
Reading: B&O 3.6
😷 masks recommended

## Slide 2: Learning Assembly
Moving data around
Arithmetic and logical operations
Control flow
Function calls
This Lecture
Reference Sheet: cs107.stanford.edu/resources/x86-64-reference.pdf
See more guides on Resources page of course website!

## Slide 3: Learning Goals
Understand how assembly implements loops and control flow
Get practice using GDB to step through assembly and examine register contents.

## Slide 4: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 5: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 6: Control Flow Review
%rip is a special register that stores the address of the next instruction to execute
We can “interfere” with %rip to change the flow of our program’s execution
jmp is one way to do this – it always jumps to the specified instruction location
Conditional jumps are another way to do this – it jumps when its condition is true
Conditional jumps work by relying on the condition codes; a set of 1-bit values that are updated by the result of the most recent arithmetic or logical operation.
cmp is commonly paired with a conditional jump to check a condition
test is another instruction that calculates bitwise & and updates condition codes

## Slide 7: Exercise 1: Conditional jump
je target jump if ZF is 1
Let %edi store 0x10. Will we jump in the following cases?
cmp $0x10,%edi je 40056f add $0x1,%edi
test $0x10,%edi je 40056f add $0x1,%edi
0x10
%edi
🤔
Input your answer on PollEv: pollev.com/cs107 or text CS107 to 22333 once to join.

## Slide 8: Exercise 1: Conditional jump
je target jump if ZF is 1
Let %edi store 0x10. Will we jump in the following cases?
cmp $0x10,%edi je 40056f add $0x1,%edi
test $0x10,%edi je 40056f add $0x1,%edi
0x10
%edi
S2 - S1 == 0, so jump
S2 & S1 != 0, so don’t jump

## Slide 9: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 10: Practice: Fill In The Blank
int if_then(int param1) {
if ( __________ ) {
_________;
}
return __________;
}
0000000000401126 <if_then>:
401126: cmp $0x6,%edi
401129: je 40112f
40112b: lea (%rdi,%rdi,1),%eax
40112e: retq
40112f: add $0x1,%edi
401132: jmp 40112b
🤔

## Slide 11: Practice: Fill In The Blank
int if_then(int param1) {
if ( __________ ) {
_________;
}
return __________;
}
0000000000401126 <if_then>:
401126: cmp $0x6,%edi
401129: je 40112f
40112b: lea (%rdi,%rdi,1),%eax
40112e: retq
40112f: add $0x1,%edi
401132: jmp 40112b
🤔
param1++
param1 * 2
param1 == 6

## Slide 12: Common If-Else Construction
long absdiff(long x, long y) {
long result;
if (x < y) {
result = y – x;
} else {
result = x – y;
}
return result;
}
Check opposite of code condition
Jump to else-body if test passes
If-body
Jump to past else-body
Else-body
Past else body
If-Else In C
If-Else In Assembly pseudocode

## Slide 13: Practice: Fill in the Blank
long absdiff(long x, long y) {
long result;
if (________) {
_________________ ;
} else {
_________________ ;
}
return result;
}
Check opposite of code condition
Jump to else-body if test passes
If-body
Jump to past else-body
Else-body
Past else body
If-Else In C
If-Else In Assembly pseudocode
401134 <+0>: mov %rsi,%rax
401137 <+3>: cmp %rsi,%rdi
40113a <+6>: jge 0x401140 <absdiff+12>
40113c <+8>: sub %rdi,%rax
40113f <+11>: retq
401140 <+12>: sub %rsi,%rdi
401143 <+15>: mov %rdi,%rax
401146 <+18>: retq
x < y
result = y - x
result = x - y
Notes: %edi – 0x3 <= 0

## Slide 14: If-Else Construction Variations
int test(int arg) {
int ret;
if (arg > 3) {
ret = 10;
} else {
ret = 0;
}
ret++;
return ret;
}
401134 <+0>: cmp $0x3,%edi
401137 <+3>: jle 0x401142 <test+14>
401139 <+5>: mov $0xa,%eax
40113e <+10>: add $0x1,%eax
401141 <+13>: retq
401142 <+14>: mov $0x0,%eax
401147 <+19>: jmp 0x40113e <test+10>
C Code
Assembly

## Slide 15: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 16: GCC Common While Loop Construction
while (test) {
body
}
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test
C
Assembly

## Slide 17: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 18: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Set %eax (i) to 0.
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 19: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Check opposite of code condition - jump if %eax is greater than 0x63. It does this by calculating %eax – 0x63 and then jg checks the resulting condition codes.
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 20: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Add 1 to %eax (i).
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 21: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Jump back to the loop test.
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 22: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
When this test is true, we jump and skip the loop body.
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 23: Loops and Control Flow
void loop() {
int i = 0;
while (i < 100) {
i++;
}
}
0x000000000040115c <+0>: mov $0x0,%eax
0x0000000000401161 <+5>: cmp $0x63,%eax
0x0000000000401164 <+8>: jg 0x40116b <loop+15>
0x0000000000401166 <+10>: add $0x1,%eax
0x0000000000401169 <+13>: jmp 0x401161 <loop+5>
0x000000000040116b <+15>: retq
Then, we return from the function.
Check opposite of code condition
Skip loop if test passes
Body
Jump back to test

## Slide 24: GCC Other While Loop Construction
while (test) {
body
}
Jump to check
Body
Check code condition
Jump to body if test passes
C
Assembly
0x0000000000400570 <+0>: mov $0x0,%eax
0x0000000000400575 <+5>: jmp 0x40057a <loop+10>
0x0000000000400577 <+7>: add $0x1,%eax
0x000000000040057a <+10>: cmp $0x63,%eax
0x000000000040057d <+13>: jle 0x400577 <loop+7>
0x000000000040057f <+15>: repz retq

## Slide 25: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 26: Common For Loop Construction
for (init; test; update) {
body
}
C For loop
Init
Check opposite of code condition
Skip loop if test passes
Body
Update
Jump back to test
Assembly pseudocode
init
while(test) {
body
update
}
C Equivalent While Loop
For loops and while loops are treated (essentially) the same when compiled down to assembly.
Notes: Add init and update

## Slide 27: GCC For Loop Output
Initialization
Jump to test
Body
Update
Test
Jump to body if success
Initialization
Test
Jump past loop if success
Body
Update
Jump to test
GCC Common For Loop Output
Possible Alternative

## Slide 28: Back to Our First Assembly
int sum_array(int arr[], int nelems) {
int sum = 0;
for (int i = 0; i < nelems; i++) {
sum += arr[i];
}
return sum;
}
0000000000401136 <sum_array>:
401136 <+0>: mov $0x0,%eax
40113b <+5>: mov $0x0,%edx
401140 <+10>: cmp %esi,%eax
401142 <+12>: jge 0x40114f <sum_array+25>
401144 <+14>: movslq %eax,%rcx
401147 <+17>: add (%rdi,%rcx,4),%edx
40114a <+20>: add $0x1,%eax
40114d <+23>: jmp 0x401140 <sum_array+10>
40114f <+25>: mov %edx,%eax
401151 <+27>: retq
Which register is C code’s sum?
Which register is C code’s i?
Which assembly instruction is C code’s sum += arr[i]?
What are the cmp and jge instructions doing? (jge: signed jump greater than/equal)
🤔

## Slide 29: Demo: GDB and Assembly
sum_array.c

## Slide 30: gdb tips
layout split
info reg
p $eax
p $eflags
b *0x400546
b *0x400550 if $eax > 98
ni
si
⭐️⭐️⭐️
View C, assembly, and gdb (lab5)
Print all registers
Print register value
Print all condition codes currently set
Set breakpoint at assembly instruction
Set conditional breakpoint
Next assembly instruction
Step into assembly instruction (will step into function calls)
(ctrl-x a: exit, ctrl-l: resize)
Notes: Refresh, ctrl-x a

## Slide 31: gdb tips
p/x $rdi
p/t $rsi
x $rdi
x/4bx $rdi
x/4wx $rdi
⭐️⭐️⭐️
Print register value in hex
Print register value in binary
Examine the byte stored at this address
Examine 4 bytes starting at this address
Examine 4 ints starting at this address

## Slide 32: Lecture Plan
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes

## Slide 33: Condition Code-Dependent Instructions
There are three common instruction types that use condition codes:
jmp instructions conditionally jump to a different next instruction
set instructions conditionally set a byte to 0 or 1
new versions of mov instructions conditionally move data

## Slide 34: set: Read condition codes
set instructions conditionally set a byte to 0 or 1.
Reads current state of flags
Destination is a single-byte register (e.g., %al) or single-byte memory location
Does not perturb other bytes of register
Typically followed by movzbl to zero those bytes
int small(int x) {
return x < 16;
}
cmp $0xf,%edi
setle %al
movzbl %al, %eax
retq

## Slide 35: set: Read condition codes
Instruction | Synonym | Set Condition (1 if true, 0 if false)
sete D | setz | Equal / zero
setne D | setnz | Not equal / not zero
sets D |  | Negative
setns D |  | Nonnegative
setg D | setnle | Greater (signed >)
setge D | setnl | Greater or equal (signed >=)
setl D | setnge | Less (signed <)
setle D | setng | Less or equal (signed <=)
seta D | setnbe | Above (unsigned >)
setae D | setnb | Above or equal (unsigned >=)
setb D | setnae | Below (unsigned <)
setbe D | setna | Below or equal (unsigned <=)

## Slide 36: cmov: Conditional move
cmovx src,dst conditionally moves data in src to data in dst.
Mov src to dst if condition x holds; no change otherwise
src is memory address/register, dst is register
May be more efficient than branch (i.e., jump)
Often seen with C ternary operator: result = test ? then: else;
int max(int x, int y) {
return x > y ? x : y;
}
cmp %edi,%esi
mov %edi, %eax
cmovge %esi, %eax
retq
Notes: Move doesn’t change flag

## Slide 37: cmov: Conditional move
Instruction | Synonym | Move Condition
cmove S,R | cmovz | Equal / zero (ZF = 1)
cmovne S,R | cmovnz | Not equal / not zero (ZF = 0)
cmovs S,R |  | Negative (SF = 1)
cmovns S,R |  | Nonnegative (SF = 0)
cmovg S,R | cmovnle | Greater (signed >) (SF = 0 and SF = OF)
cmovge S,R | cmovnl | Greater or equal (signed >=) (SF = OF)
cmovl S,R | cmovnge | Less (signed <) (SF != OF)
cmovle S,R | cmovng | Less or equal (signed <=) (ZF = 1 or SF! = OF)
cmova S,R | cmovnbe | Above (unsigned >) (CF = 0 and ZF = 0)
cmovae S,R | cmovnb | Above or equal (unsigned >=) (CF = 0)
cmovb S,R | cmovnae | Below (unsigned <) (CF = 1)
cmovbe S,R | cmovna | Below or equal (unsigned <=) (CF = 1 or ZF = 1)

## Slide 38: Last Lab: Conditional Move
int signed_division(int x) {
return x / 4;
}
signed_division:
leal 3(%rdi), %eax
testl %edi, %edi
cmovns %edi, %eax
sarl $2, %eax
ret
Put x + 3 into %eax
Check the sign of x
If x is nonnegative, put x into %eax
Divide %eax by 4

## Slide 39: Optimizations
Conditional Moves can sometimes eliminate “branches” (jumps), which are particularly inefficient on modern computer hardware.
Processors try to predict the future execution of instructions for maximum performance. This is difficult to do with jumps.
This is called branch prediction / speculative execution
The Spectre vulnerability exploited an issue with this on modern processors to access protected information
Processors may also use out-of-order execution (look ahead)
The Meltdown vulnerability exploited an issue with out-of-order execution on modern processors to access protected data
https://meltdownattack.com

## Slide 40: Recap
Recap: Control Flow Mechanics
If statements
Loops
  While loops
  For loops
Other Instructions That Depend On Condition Codes
Lecture 19 takeaway: Loops and conditionals commonly use cmp or test along with jumps to conditionally skip over or repeat assembly instructions. We can use GDB to step through individual assembly instructions and view register contents.

## Slide 41: Practice: Fill in the blanks
<+0>: mov $0x1,%eax
<+5>: cmp %rsi,%rdi
<+8>: jge 0x1151 <loop+24>
<+10>: lea (%rdi,%rsi,1),%rdx
<+14>: imul %rdx,%rax
<+18>: add $0x1,%rdi
<+22>: jmp 0x113e <loop+5>
<+24>: retq
long loop(long a, long b) {
long result = ___(1)___;
while (___(2)___) {
result = ____(3)_____;
a = ___(4)___;
}
return result;
}
🤔
GCC common while loop construction:
Test
Jump past loop if fails
Body
Jump to test
https://godbolt.org/z/zrW6c5MGa

## Slide 42: Practice: Fill in the blanks
<+0>: mov $0x1,%eax
<+5>: cmp %rsi,%rdi
<+8>: jge 0x1151 <loop+24>
<+10>: lea (%rdi,%rsi,1),%rdx
<+14>: imul %rdx,%rax
<+18>: add $0x1,%rdi
<+22>: jmp 0x113e <loop+5>
<+24>: retq
long loop(long a, long b) {
long result = ___(1)___;
while (___(2)___) {
result = ____(3)_____;
a = ___(4)___;
}
return result;
}
🤔
GCC common while loop construction:
Test
Jump past loop if fails
Body
Jump to test

## Slide 43: Practice: Fill in the blanks
<+0>: mov $0x1,%eax
<+5>: cmp %rsi,%rdi
<+8>: jge 0x1151 <loop+24>
<+10>: lea (%rdi,%rsi,1),%rdx
<+14>: imul %rdx,%rax
<+18>: add $0x1,%rdi
<+22>: jmp 0x113e <loop+5>
<+24>: retq
long loop(long a, long b) {
long result = _________;
while (_________) {
result = ____________;
a = _________;
}
return result;
}

## Slide 44: Practice: Fill in the blanks
long loop(long a, long b) {
long result = _________;
while (_________) {
result = ____________;
a = _________;
}
return result;
}
1
a < b
result*(a+b)
a + 1
<+0>: mov $0x1,%eax
<+5>: cmp %rsi,%rdi
<+8>: jge 0x1151 <loop+24>
<+10>: lea (%rdi,%rsi,1),%rdx
<+14>: imul %rdx,%rax
<+18>: add $0x1,%rdi
<+22>: jmp 0x113e <loop+5>
<+24>: retq

## Slide 45: test practice: What’s the C code?
0x400546 <test_func> test %edi,%edi
0x400548 <test_func+2> jns 0x400550 <test_func+10>
0x40054a <test_func+4> mov $0xfeed,%eax
0x40054f <test_func+9> retq
0x400550 <test_func+10> mov $0xaabbccdd,%eax
0x400555 <test_func+15> retq
🤔

## Slide 46: test practice: What’s the C code?
0x400546 <test_func> test %edi,%edi
0x400548 <test_func+2> jns 0x400550 <test_func+10>
0x40054a <test_func+4> mov $0xfeed,%eax
0x40054f <test_func+9> retq
0x400550 <test_func+10> mov $0xaabbccdd,%eax
0x400555 <test_func+15> retq
int test_func(int x) {
if (x < 0) {
return 0xfeed;
}
return 0xaabbccdd;
}
(or anything like this)

## Slide 47: Practice: “Escape Room”
<escape_room+0> lea (%rdi,%rdi,1),%eax
<escape_room+3> cmp $0x5,%eax
<escape_room+6> jg 0x114c <escape_room+19>
<escape_room+8> cmp $0x1,%edi
<escape_room+11> je 0x1152 <escape_room+25>
<escape_room+13> mov $0x0,%eax
<escape_room+18> retq
<escape_room+19> mov $0x1,%eax
<escape_room+24> retq
<escape_room+25> mov $0x1,%eax
<escape_room+30> retq
What must be passed to the escapeRoom function such that it returns true (1) and not false (0)?
You don’t have to reverse-engineer C code exactly! Just figure out the big picture!

## Slide 48: Practice: “Escape Room”
<escape_room+0> lea (%rdi,%rdi,1),%eax
<escape_room+3> cmp $0x5,%eax
<escape_room+6> jg 0x114c <escape_room+19>
<escape_room+8> cmp $0x1,%edi
<escape_room+11> je 0x1152 <escape_room+25>
<escape_room+13> mov $0x0,%eax
<escape_room+18> retq
<escape_room+19> mov $0x1,%eax
<escape_room+24> retq
<escape_room+25> mov $0x1,%eax
<escape_room+30> retq
First param > 2 or == 1.
What must be passed to the escapeRoom function such that it returns true (1) and not false (0)?

## Slide 49: Exercise 2: Conditional jump
What is the value of %rip after executing the jne instruction?
  4004d9
  4004db
  4004de
  Other
0x5
%edi
00000000004004d6 <if_then>:
4004d6: 83 ff 06 cmp $0x6,%edi
4004d9: 75 03 jne 4004de <if_then+0x8>
400rdb: 83 c7 01 add $0x1,%edi
4004de: 8d 04 3f lea (%rdi,%rdi,1),%eax
4004e1: c3 retq
🤔
What is the value of %eax when we hit the retq instruction?
  4004e1
  0x2
  0xa
  0xc
  Other
Notes: 0x5 - 0x6 = -1 != 0
1. C: %rip: 4004de (i.e., do not add 1)
2. C: 5 + 1 * 5 = 10 = 0xa

## Slide 50: Exercise 2: Conditional jump
What is the value of %eax when we hit the retq instruction?
  4004e1
  0x2
  0xa
  0xc
  Other
What is the value of %rip after executing the jne instruction?
  4004d9
  4004db
  4004de
  Other
0x5
%edi
00000000004004d6 <if_then>:
4004d6: 83 ff 06 cmp $0x6,%edi
4004d9: 75 03 jne 4004de <if_then+0x8>
400rdb: 83 c7 01 add $0x1,%edi
4004de: 8d 04 3f lea (%rdi,%rdi,1),%eax
4004e1: c3 retq
Notes: 0x5 - 0x6 = -1 != 0
1. C: %rip: 4004de (i.e., do not add 1)
2. C: 5 + 1 * 5 = 10 = 0xa