## Slide 1
EE 359: Wireless Communications
Professor Andrea Goldsmith
Next-Gen Cellular/WiFi
Smart Homes/Spaces
Autonomous Cars
Smart Cities
Body-Area Networks
Internet of Things
All this and more …

## Slide 2: About me
Engineering prof dad, cartoonist mom
Undergrad at UC Berkeley 1982-1986
Worked in Silicon Valley 1986-1989
Fell in love with wireless.
Ph.D. from UCB: 1989-1994
  Summers at AT&T Bell Labs
Taught at Caltech 1994-1999
Moved to Stanford in 1999
  Lots of stuff in addition to research, teaching
Founded 2 wireless companies: Quantenna (QTNA’06) and Plume WiFi’10 Much work around diversity in STEM (in academia, industry, and IEEE)
Best Results: Daniel (22) and Nicole (20)

## Slide 3: Outline
Course Basics
Course Syllabus
Wireless History
The Wireless Vision
Technical Challenges
Current/Next-Gen Wireless Systems
Spectrum Regulation and Standards
Emerging Wireless Systems (Optional Lecture)

## Slide 4: Course Information* People
Instructor: Andrea Goldsmith, Pack 371, andrea@ee, OHs: TTh immediately after class and by appt.
TA: Tom Dean (trdean@stanford.edu)
  Discussion section: Wed 4-5 pm (hopefully taped)
  OHs: Wed 5-6pm, Th 4-5pm, Fri 11-12pm (tentative). Emails received during OHs will be responded to during or just after. Email questions are ideally via Piazza.
  Piazza: https://piazza.com/stanford/win2020/ee359/home. All are registered, will use to poll on OH/discussion times
Class Administrator: Dash Corbett, email: dashiellcorbett@stanford.edu, 365 Packard, 723-2681. Homework dropoff: Fri by 4 pm.
*See web or handout for more details

## Slide 5: Course Information Nuts and Bolts
Prerequisites: EE279 or equivalent (Digital Communications)
Textbook: Wireless Communications (by me), draft 2nd Ed.
  Available as reader at bookstore or on website
  Raffle for $100 Amazon gift card for typos/mistakes/suggestions
  Supplemental texts at Engineering Library.
Class Homepage: www.stanford.edu/class/ee359
  All announcements, handouts, homeworks, etc. posted to website
  “Lectures” link continuously updates topics, handouts, and reading
  Calendar will show any changes to class/OH/discussion times
Class Mailing List: ee359-win1920-students@lists (automatic for on-campus registered students).
  Guest list ee359-win1920-guest@lists for SCPD and auditors: send Tom email to sign up.
  Sending mail to ee359-win1920-staff@lists reaches me and Tom.

## Slide 6
Grading: Two Options
  No Project (3 units): HW – 25%, 2 Exams – 35%, 40%
  Project (4 units): HWs- 20%, Exams - 25%, 30%, Project - 25%
HWs: assigned Thu, due following Fri 4pm (starts next week)
  Homeworks lose 33% credit after 4pm Fri, lowest HW dropped
  Up to 3 students can collaborate and turn in one HW writeup
  Collaboration means all collaborators work out all problems together
  Unpermitted collaboration or aid (e.g. solns for the book or from prior years) is an honor code violation and will be dealt with strictly.
  Extra credit: up to 2 “design your own” HW problems; course eval
Exams:
  Midterm week of 2/17 (It will be scheduled outside class time; the duration is 2 hours.) Final on 3/17 from 3:30-6:30pm (pizza after)
  Exams must be taken at scheduled time (with very few exceptions)
Course Information Policies

## Slide 7
The term project (for students electing to do a project) is a research project related to any topic in wireless
Two people may collaborate if you convince me the sum of the parts is greater than each individually
A 1 page proposal is due 2/7 at midnight.
  5-10 hours of work typical for proposal
  Must create project website and post proposal there (submit web link)
  Preliminary proposals can be submitted for early feedback
The project is due by midnight on 3/14 (on website)
  20-40 hours of work after proposal is typical for a project
Suggested topics in project handout
  Anything related to wireless or application of wireless techniques ok.
Course Information Projects

## Slide 8: Course Syllabus
Overview of Wireless Communications
Path Loss, Shadowing, and Fading Models
Capacity of Wireless Channels
Digital Modulation and its Performance
Adaptive Modulation
Diversity
MIMO Systems
Multicarrier Systems: OFDM and other waveforms
Multiuser and Cellular Systems

## Slide 9: Tentative Detailed Syllabus
Lecture # | Date | Topic | Required Reading | 
 |  | Introduction |  | 
1 | 1/7 | Overview of Wireless Communications | Chapter 1 | 
Wireless Channel Models |  |  |  | 
2-3 | 1/9, 1/14 | Path Loss and Shadowing Models, Millimeter wave propagation | Chapter 2 | 
4-5 | 1/17, 1/21 | Statistical Fading Models, Narrowband Fading | Section 3.1-3.2.3 | 
6 | 1/23 | Wideband Fading Models | Section 3.3 | 
Impact of Fading and ISI on Wireless Performance |  |  |  | 
7 | 1/28 | Capacity of Wireless Channels |  | Chapter 4
8,9,10 | 1/30, 2/5, 2/6 | Digital Modulation and its Performance |  | Lec 8: Chapter 5 Lec 9-10: Chapter 6
Flat-Fading Countermeasures |  |  |  | 
11 | 2/11 | Diversity |  | Chapter 7
MT | Week of 2/17 | Midterm (outside class time) | Chapters 2 to 7 | 
12-13 | 2/13-2/18 | Adaptive Modulation |  | Chapter 9.1-9.3
14-15 | 2/21-2/25 | Multiple Input/Output Systems (MIMO) | Chapter 10, Appendix C | 
ISI Countermeasures |  |  |  | 
16-17 | 2/27, 3/3 | Multicarrier Systems, OFDM, and other multicarrier waveforms | Chapter 12 | 
18-19 | 3/4-3/10 | Multiuser and Cellular Systems | Topics in Chapters 13-15 | 
Course Summary |  |  |  | 
20 | 3/12 | Course summary/final review (and optional advanced topics lecture over lunch) |  | 
Final | 3/17 | 3:30-6:30pm | Pizza party to follow | 

## Slide 10: Class Rescheduling
No lectures Thu 1/16, Tue 2/4, Thu 2/20 and Thu 3/5.
These lectures are tentatively rescheduled as:
  Lecture on Thu 1/16 is rescheduled to Fri 1/17 at lunch
  Lecture on Tue 2/4 is rescheduled to Wed 2/5 at lunch
  Lecture on Thu 2/20 is rescheduled to Fri 2/21 at lunch
  Lecture on Thu 3/5 is rescheduled to Wed 3/4 at lunch
Last lecture on 3/12 has an optional component 11:50-12:30 on advanced topics with lunch.

## Slide 11: Wireless History
Radio invented in the 1880s by Marconi
Many sophisticated military radio systems were developed during and after WW2
Wifi also enjoying tremendous success and growth
Bluetooth pervasive, satellites also widespread
Ancient Systems: Smoke Signals, Carrier Pigeons, …
Exponential growth in cellular use since 1988: approx. 8B worldwide users today
  Ignited the wireless revolution
  Voice, data, and multimedia ubiquitous
  Use in 3rd world countries growing rapidly

## Slide 12: Future Wireless Networks
Ubiquitous Communication Among People and Devices
Next-Gen Cellular/WiFi
Smart Homes/Spaces
Autonomous Cars
Smart Cities
Body-Area Networks
Internet of Things
All this and more …

## Slide 13: Challenges
Cellular
Mem
BT
CPU
GPS
WiFi
mmW
Cog
Radio
Network/Radio Challenges
  Gbps data rates with “no” errors
  Energy efficiency
  Scarce/bifurcated spectrum
  Reliability and coverage
  Heterogeneous networks
  Seamless internetwork handoff
AdHoc
Short-Range
5-6G
Device/SoC Challenges
  Performance
  Complexity
  Size, Power, Cost, Energy
  High frequencies/mmWave
  Multiple Antennas
  Multiradio Integration
  Coexistance

## Slide 14: Software-Defined (SD) Radio:
Wideband antennas and A/Ds span BW of desired signals
DSP programmed to process desired signal: no specialized HW
Cellular
Apps
Processor
BT
Media
Processor
GPS
WLAN
Wimax
DVB-H
FM/XM
A/D
A/D
DSP
A/D
A/D
Is this the solution to the device challenges?
Today, this is not cost, size, or power efficient
SubNyquist sampling may help with the A/D and DSP requirements

## Slide 15: “Sorry America, your airwaves are full*”
Exponential Mobile Data Growth
Leading to massive spectrum deficit
Source: FCC

## Slide 16: On the Horizon, the Internet of Things

## Slide 17
What is the Internet of Things:
Different requirements than smartphones: low rates/energy consumption
Enabling every electronic device to be connected to each other and the Internet
Includes smartphones, consumer electronics, cars, lights, clothes, sensors, medical devices,…
Value in IoT is data processing in the cloud

## Slide 18
  “Effectively unlimited” capacity possible via personal cells (pcells). S. Perlman, Artemis.
  “The wireless industry has reached the theoretical limit of how fast networks can go” K. Fitcher, Connected Planet
  “There is no theoretical maximum to the amount of data that can be carried by a radio channel” M. Gass, 802.11 Wireless Networks: The Definitive Guide
  “We’re 99% of the way” to the “barrier known as Shannon’s limit,” D. Warren, GSM Association Sr. Dir. of Tech.
Shannon was wrong, there is no limit
We are at the Shannon Limit
Are we at the Shannon limit of the Physical Layer?

## Slide 19: What would Shannon say?
  Time-varying channels.
We don’t know the Shannon capacity of most wireless channels
  Channels with interference or relays.
  Cellular systems
  Channels with delay/energy/$$$ constraints.
  Ad-hoc and sensor networks
Shannon theory provides design insights
and system performance upper bounds

## Slide 20: Current/Next-Gen Wireless Systems
Current:
  4G Cellular Systems (LTE-Advanced)
  6G Wireless LANs/WiFi (802.11ax)
  mmWave massive MIMO systems
  Satellite Systems
  Bluetooth
  Zigbee
  WiGig
Emerging
  5G Cellular and 7G WiFi Systems
  Ad/hoc and Cognitive Radio Networks
  Energy-Harvesting Systems
  Chemical/Molecular
Much room
For innovation

## Slide 21: Spectral Reuse
Due to its scarcity, spectrum is reused
BS
In licensed bands
Cellular
Wifi, BT, UWB,…
and unlicensed bands
Reuse introduces interference

## Slide 22: Cellular Systems: Reuse channels to maximize capacity
Geographic region divided into cells
Freq./timeslots/codes/space reused in different cells (reuse 1 common).
Interference between cells using same channel: interference mitigation key
Base stations/MTSOs coordinate handoff and control functions
Shrinking cell size increases capacity, as well as complexity, handoff, …
BASE
STATION
MTSO

## Slide 23: 4G/LTE Cellular
Much higher data rates than 3G (50-100 Mbps)
  3G systems has 384 Kbps peak rates
Greater spectral efficiency (bits/s/Hz)
  More bandwidth, adaptive OFDM-MIMO, reduced interference
Flexible use of up to 100 MHz of spectrum
  10-20 MHz spectrum allocation common
Low packet latency (<5ms).
Reduced cost-per-bit (not clear to customers)
All IP network

## Slide 24: 5G Upgrades from 4G

## Slide 25: Future Cellular Phones
Much better performance and reliability than today
- Gbps rates, low latency, 99% coverage, energy efficiency
BS
BS
Phone
System
BS
San Francisco
Paris
Nth-Gen
Cellular
Nth-Gen
Cellular
Internet
LTE backbone is the Internet
Everything wireless in one device
Burden for this performance is on the backbone network

## Slide 26: Wifi Networks Multimedia Everywhere, Without Wires
802.11ac
Wireless HDTV
and Gaming
Streaming video
Gbps data rates
High reliability
Coverage inside and out

## Slide 27: Wireless LAN Standards
802.11b (Old – 1990s)
  Standard for 2.4GHz ISM band (80 MHz)
  Direct sequence spread spectrum (DSSS)
  Speeds of 11 Mbps, approx. 500 ft range
802.11a/g (Middle Age– mid-late 1990s)
  Standard for 5GHz band (300 MHz)/also 2.4GHz
  OFDM in 20 MHz with adaptive rate/codes
  Speeds of 54 Mbps, approx. 100-200 ft range
802.11n/ac/ax or Wi-Fi 6 (current gen)
  Standard in 2.4 GHz and 5 GHz band
  Adaptive OFDM /MIMO in 20/40/80/160 MHz
  Antennas: 2-4, up to 8
  Speeds up to 1 Gbps (10 Gbps for ax), approx. 200 ft range
  Other advances in packetization, antenna use, multiuser MIMO
Many
WLAN
cards
have many generations

## Slide 28: Why does WiFi performance suck?
The WiFi standard lacks good mechanisms to mitigate interference, especially in dense AP deployments
  Multiple access protocol (CSMA/CD) from 1970s
  Static channel assignment, power levels, and sensing thresholds
  In such deployments WiFi systems exhibit poor spectrum reuse and significant contention among APs and clients
    Result is low throughput and a poor user experience
  Multiuser MIMO will help each AP, but not interfering APs
Carrier Sense Multiple Access:
if another WiFi signal
detected, random backoff
Collision Detection: if collision
detected, resend

## Slide 29: Self-Organizing Networks for WiFi
SoN-for-WiFi: dynamic self-organization network software to manage of WiFi APs.
Allows for capacity/coverage/interference mitigation tradeoffs.
Also provides network analytics and planning.
SoN
Controller
- Channel Selection
- Power Control
- etc.

## Slide 30: Satellite Systems
Cover very large areas
Different orbit heights
  Orbit height trades off coverage area for latency
  GEO (39000 Km) vs MEO (9000 km) vs LEO (2000 Km)
Optimized for one-way transmission
  Radio (XM, Sirius) and movie (SatTV, DVB/S) broadcasts
  Most two-way LEO systems went bankrupt in 1990s-2000s
  LEOs have resurfaced with 4G to bridge digital divide
Global Positioning System (GPS) ubiquitous
  Satellite signals used to pinpoint location
  Popular in cell phones, PDAs, and navigation devices

## Slide 31: Bluetooth
8C32810.61-Cimini-7/98
Cable replacement RF technology (low cost)
Short range (10m, extendable to 100m)
2.4 GHz band (crowded)
1 Data (700 Kbps) and 3 voice channels, up to 3 Mbps
Widely supported by telecommunications, PC, and consumer electronics companies
Few applications beyond cable replacement

## Slide 32: IEEE 802.15.4/ZigBee Radios
Low-rate low-power low-cost secure radio
  Complementary to WiFi and Bluetooth
Frequency bands: 784, 868, 915 MHz, 2.4 GHz
Data rates: 20Kbps, 40Kbps, 250 Kbps
Range: 10-100m line-of-sight
Support for large mesh networking or star clusters
Support for low latency devices
CSMA-CA channel access
Applications: light switches, electricity meters, traffic management, and other low-power sensors.

## Slide 33: Spectrum Regulation
Spectrum a scarce public resource, hence allocated
Spectral allocation in US controlled by FCC (commercial) or OSM (defense)
FCC auctions spectral blocks for set applications.
Some spectrum set aside for universal use
Worldwide spectrum controlled by ITU-R
Regulation is a necessary evil.
Innovations in regulation being considered worldwide
in multiple cognitive radio paradigms

## Slide 34: Standards
Interacting systems require standardization
Companies want their systems adopted as standard
  Alternatively try for de-facto standards
Standards determined by TIA/CTIA in US
  IEEE standards often adopted
  Process fraught with inefficiencies and conflicts
Worldwide standards determined by ITU-T
  In Europe, ETSI is equivalent of IEEE
Standards for current systems summarized in text Appendix D.

## Slide 35: Emerging Systems
New cellular system architectures
mmWave/massive MIMO communications
Software-defined network architectures
Ad hoc/mesh wireless networks
Cognitive radio networks
Wireless sensor networks
Energy-constrained radios
Distributed control networks
Chemical Communications
Applications of Communications in Health, Bio-medicine, and Neuroscience
Advanced Topics Lecture: See Backup Slides

## Slide 36: Main Points
The wireless vision encompasses many exciting applications
Technical challenges transcend all system design layers
5G networks must support higher performance for some users, extreme energy efficiency and/or low latency for others
Cloud-based software to dynamically control and optimize wireless networks needed (SDWN)
Innovative wireless design needed for 5G cellular/WiFi, mmWave systems, massive MIMO, and IoT connectivity
Standards and spectral allocation heavily impact the evolution of wireless technology

## Slide 37: Backup Slides: Emerging Systems

## Slide 38: Rethinking “Cells” in Cellular
Traditional cellular design “interference-limited”
  MIMO/multiuser detection can remove interference
  Cooperating BSs form a MIMO array: what is a cell?
  Relays change cell shape and boundaries
  Distributed antennas move BS towards cell boundary
  Small cells create a cell within a cell
  Mobile cooperation via relays, virtual MIMO, network coding.
Small
Cell
Relay
DAS
Coop
MIMO
How should cellular
systems be designed for
Capacity
Coverage
Energy efficiency
Low latency

## Slide 39: mmWave Massive MIMO
mmWaves have large non-monotonic path loss
  Channel model poorly understood
For asymptotically large arrays with channel state information, no attenuation, fading, interference or noise
mmWave antennas are small: perfect for massive MIMO
Bottlenecks: channel estimation and system complexity
Non-coherent design holds significant promise
Hundreds
of antennas
Dozens of devices
10s of GHz of Spectrum

## Slide 40: Software-Defined Network Architectures
Freq.
Allocation
Power
Control
Self
Healing
ICIC
QoS
Opt.
CS
Threshold
UNIFIED CONTROL PLANE
Network Optimization
App layer
Video
Security
Vehicular
Networks
Health
M2M
WiFi
Cellular
mmWave
Ad-Hoc
Networks
HW layer
…
Distributed Antennas
Cloud Computing

## Slide 41: Ad-Hoc Networks
Peer-to-peer communications
  No backbone infrastructure or centralized control
Routing can be multihop.
Topology is dynamic.
Fully connected with different link SINRs
Open questions
  Fundamental capacity region
  Resource allocation (power, rate, spectrum, etc.)
  Routing
Notes: -No backbone: nodes must self-configure into a network.
-In principle all nodes can communicate with all other nodes, but multihop routing can reduce the interference associated with direct transmission.
-Topology dynamic since nodes move around and link characteristics change.
-Applications: appliances and entertainment units in the home, community networks that bypass the Internet. Military networks for robust flexible easily-deployed network (every soldier is a node).

## Slide 42: Cognitive Radios
Cognitive radios support new users in existing crowded spectrum without degrading licensed users
  Utilize advanced communication and DSP techniques
  Coupled with novel spectrum allocation policies
Multiple paradigms
  (MIMO) Underlay (interference below a threshold)
  Interweave finds/uses unused time/freq/space slots
  Overlay (overhears/relays primary message while cancelling interference it causes to cognitive receiver)
NCR
IP
NCR
CR
CR
CRRx
NCRRx
NCRTx
CRTx
MIMO Cognitive Underlay
Cognitive Overlay

## Slide 43
Wireless Sensor Networks
Data Collection and Distributed Control
Energy (transmit and processing) is the driving constraint
Data flows to centralized location (joint compression)
Low per-node rates but tens to thousands of nodes
Intelligence is in the network rather than in the devices
Smart homes/buildings
Smart structures
Search and rescue
Homeland security
Event detection
Battlefield surveillance

## Slide 44: Energy-Constrained Radios
Transmit energy minimized by sending bits slowly
  Leads to increased circuit energy consumption
Short-range networks must consider both transmit and processing/circuit energy.
  Sophisticated encoding/decoding not always energy-efficient.
  MIMO techniques not necessarily energy-efficient
  Long transmission times not necessarily optimal
  Multihop routing not necessarily optimal
  Sub-Nyquist sampling can decrease energy and is sometimes optimal!
Notes: All the sophisticated high-performance communication techniques developed since WW2 may need to be thrown out the window.
By cooperating, nodes can save energy

## Slide 45: Where should energy come from?
Batteries and traditional charging mechanisms
  Well-understood devices and systems
Wireless-power transfer
  Poorly understood, especially at large distances and with high efficiency
Communication with Energy Harvesting Radios
  Intermittent and random energy arrivals
  Communication becomes energy-dependent
  Can combine information and energy transmission
  New principles for radio and network design needed.

## Slide 46
Distributed Control over Wireless
  Interdisciplinary design approach
    Control requires fast, accurate, and reliable feedback.
    Wireless networks introduce delay and loss
    Need reliable networks and robust controllers
    Mostly open problems
Automated Vehicles
- Cars
- Airplanes/UAVs
- Insect flyers
: Many design challenges

## Slide 47: Chemical Communications
Can be developed for both macro (>cm) and micro (<mm) scale communications
Greenfield area of research:
  Need new modulation schemes, channel impairment mitigation, multiple acces, etc.

## Slide 48: Applications in Health, Biomedicine and Neuroscience
Recovery from Nerve Damage
Neuroscience
Nerve network (re)configuration
EEG/ECoG signal processing
Signal processing/control for deep brain stimulation
SP/Comm applied to bioscience
Body-Area
Networks
ECoG Epileptic Seizure Localization
EEG
ECoG