## Slide 1: EE359 – Lecture 18 Outline
Announcements
  HW due Fri; last HW posted, due Sunday 12/10 at 4 pm (no late HWs)
  Lecture next Thu 12/7 10-11:50 (course review+advanced topics)
  Final info (coverage, format, extra OHs, etc) given in 12/5 lecture
  Final exam 12/13, 12:15pm-3:15pm in Thornton 102
  Final projects must be posted 12/9 at midnight.
Spread Spectrum
  Direct sequence (DSSS)
  ISI and Interference Rejection of DSSS
  RAKE Receiver
Multiuser Systems
  Multiple access techniques
  Random access techniques

## Slide 2: Review of Last Lecture MCM, Overlapping Subcarriers and FFT Implementation (OFDM)
  MCM splits high rate data stream into lower rate flat-fading substreams
  Overlapping subcarriers reduces BW by factor of 2
  Modulate symbols with IFFT at TX, Reverse structure (with FFT) in RX
  Cyclic prefix makes linear convolution of channel circular, so no interference between FFT blocks in RX processing
x
cos(2pfct)
R bps
QAM
Modulator
Serial
To
Parallel
Converter
IFFT
X0
XN-1
x0
xN-1
Add cyclic
prefix and
Parallel
To Serial
Convert
D/A
TX
x
cos(2pfct)
R bps
QAM
Modulator
FFT
Y0
YN-1
y0
yN-1
Remove
cyclic
prefix and
Serial to
Parallel
Convert
A/D
LPF
Parallel
To Serial
Convert
RX
Yi=HiXi+ni
h(t)
+
n(t)

## Slide 3: Review Continued OFDM Design Issues
Timing/frequency offset:
  Impacts subcarrier orthogonality; self-interference
Peak-to-Average Power Ratio (PAPR)
  Adding subcarrier signals creates large signal peaks
  Solve with clipping or PAPR-optimized coding
Mitigation for fading across subcarriers
  Precoding (fading inversion): Used in DSL as there is minimal deep fades, not used in wireless systems
  Adaptive modulation: data rate (and power) adapted to subcarrier SNR. Used in LTE and 802.11a-g-n-ac
  Coding across subcarriers: bits are encoded into a block code of length N for N subcarriers. Each coded symbol is sent on a different subcarrier.

## Slide 4: Intro. to Spread Spectrum
Modulation that increases signal bandwidth
  Spreads modulated signal over wider BW B~1/Ts than needed for transmission (R=log2(M)/Ts)
  Mitigates or coherently combines ISI
  Mitigates narrowband interference/jamming
  Hides signal below noise (DSSS) or makes it hard to track (FH)
  Also used as a multiple access technique
Two types
  Frequency Hopping:
    Narrowband signal hopped over wide bandwidth
  Direction Sequence:
    Modulated signal multiplied by faster chip sequence

## Slide 5: Direct Sequence Spread Spectrum
Bit sequence modulated by chip sequence
Spreads bandwidth by large factor (G)
Despread by multiplying by sc(t) again (sc(t)=1)
Mitigates ISI and narrowband interference
s(t)
sc(t)
Tb=KTc
Tc
S(f)
Sc(f)
1/Tb
1/Tc
S(f)*Sc(f)
2

## Slide 6: ISI and Interference Rejection
Narrowband Interference Rejection (1/K)
Multipath Rejection (Autocorrelation r(t))
S(f)
S(f)
I(f)
S(f)*Sc(f)
Info. Signal
Receiver Input
Despread Signal
I(f)*Sc(f)
S(f)
aS(f)
S(f)*Sc(f)[ad(t)+b(t-t)]
Info. Signal
Receiver Input
Despread Signal
brS’(f)
Can coherently combine all multipath components via a RAKE receiver

## Slide 7: RAKE Receiver
Multibranch receiver
  Branches synchronized to different MP components
These components can be coherently combined
  Use SC, MRC, or EGC
x
x
sc(t)
sc(t-iTc)
x
sc(t-NTc)
Demod
Demod
Demod
y(t)
Diversity
Combiner
dk
^

## Slide 8: Multiuser Channels: Uplink and Downlink
Downlink (Broadcast Channel or BC):
One Transmitter
to Many Receivers.
Uplink (Multiple Access
Channel or MAC):
Many Transmitters
to One Receiver.
R1
R2
R3
x
h1(t)
x
h21(t)
x
h3(t)
x
h22(t)
Uplink and Downlink typically duplexed in time or frequency
Full-duplex radios are being considered for 5G systems

## Slide 9: Bandwidth Sharing in Multiple Access Channels assigned by central controller
7C29822.033-Cimini-9/97
Frequency Division
  OFDMA
Time Division
Code Division
  Code cross-correlation dictates interference
  Multiuser Detection
Space Division (SDMA)
Hybrid Schemes
Code Space
Time
Frequency
  Code Space
Time
Frequency
Code Space
Time
Frequency

## Slide 10
Random vs. Multiple Access
• In multiple access, channels are assigned by a centralized controller
- Requires a central controller and control channel
- Inefficient for short and/or infrequent data transmissions
In random access, users access channel randomly when they have data to send
  A simple random access scheme will be explored in homework
• Pure ALOHA
– send packet whenever data is available
– a collision occurs for any partial overlap of
• Slotted ALOHA
– packets sent during predefined timeslots
– A collision occurs when packets overlap,
but there is no partial overlap of packets
– Packets received in error are retransmitted
after random delay interval.
packets (nonorthogonal slots)
– Packets received in error are retransmitted after random delay interval (avoids subsequent collisions).
• ALOHA Schemes (not on exams/HW)
  Data is packetized.
  Packets occupy a given time interval
– same as ALOHA but with packet slotting

## Slide 11: Main Points
Spread spectrum increases signal bandwidth above that required for information transmission
Benefits of spread spectrum:
  ISI/narrowband interference rejection by spreading gain
  Also used as a multiuser/multiple access technique
Multiple access: users can share the same spectrum via time/frequency/code/space division
Random access more efficient than multiple access for short/infrequent data transmission