## Slide 1: EE359 – Lecture 6 Outline
Announcements:
  HW due tomorrow 4pm
  Makeup lecture next Friday, Oct. 20, 10:30-11:50 in this room
Review of Last Lecture
Wideband Multipath Channels
Scattering Function
Multipath Intensity Profile
Doppler Power Spectrum

## Slide 2: Review of Last Lecture
  For fn~U[0,2p], rI(t),rQ(t) zero mean, WSS, with
Uniform AoAs in Narrowband Model
  In-phase/quad comps have zero cross correlation and
PSD maximum at the maximum Doppler frequency
    PSD used to generate simulation values
Decorrelates over roughly half a wavelength
.4l
vt=d
fc+fD
Sr(f)
fc
fc-fD
1
fD=v/l

## Slide 3: Review Continued: Signal Envelope Distribution
CLT approx. leads to Rayleigh distribution (power is exponential)
When LOS component present, Ricean distribution is used
Measurements support Nakagami distribution in some environments
  Similar to Ricean, but models “worse than Rayleigh”
  Lends itself better to closed form BER expressions
To cover today

## Slide 4: Wideband Channels
Individual multipath components resolvable
True when time difference between components exceeds signal bandwidth
  High-speed wireless systems are wideband for most environments
t
t
Narrowband
Wideband

## Slide 5: Scattering Function
Typically characterize c(t,t) by its statistics, since it is a random process
Underlying process WSS and Gaussian, so only characterize mean (0) and correlation
Autocorrelation is Ac(t1,t2,Dt)=Ac(t,Dt)
  Correlation for single mp delay/time difference
Statistical scattering function:
  Average power for given mp delay and doppler
t
r
s(t,r)=FDt[Ac(t,Dt)]
Easy to measure

## Slide 6: Multipath Intensity Profile
Defined as Ac(t,Dt=0)= Ac(t)
  Determines average (mTm ) and rms (sTm) delay spread
  Approximates maximum delay of significant multipath
Coherence bandwidth Bc=1/sTm
  Maximum frequency over which Ac(Df)=F[Ac(t)]>0
  Ac(Df)=0 implies signals separated in freq. by Df will be uncorrelated after going through channel: freq. distortion
t
Ac(t)
TM
t
f
Ac(f)
0
Bc
Wideband signal
distorted in time and in frequency

## Slide 7: Doppler Power Spectrum
Doppler Power Spectrum: Sc(r)=FDt [Ac(Df=0,Dt)Ac(Dt)]
  Power of multipath at given Doppler
  Doppler spread Bd: Max. doppler for which Sc (r)=>0.
  Coherence time Tc=1/Bd: Max time over which Ac(Dt)>0
    Ac(Dt)=0 signals separated in time by Dt uncorrelated after passing through channel
Why do we look at Doppler w.r.t. Ac(Df=0,Dt)?
  Captures Doppler associated with a narrowband signal
  Autocorrelation over a narrow range of frequencies
  Fully captures time-variations, multipath angles of arrival
Ac(Df,Dt)=Ft[Ac(t,Dt)]
r
Sc(r)
Bd
Scattering Function: s(t,r)=FDt[Ac(t,Dt)]

## Slide 8: Main Points
Wideband channels have resolvable multipath
  Statistically characterize c(t,t) for WSSUS model
  Scattering function characterizes rms delay and Doppler spread. Key parameters for system design.
Delay spread defines maximum delay of significant multipath components. Inverse is coherence BW
  Signal distortion in time/freq. when delay spread exceeds inverse signal BW (signal BW exceeds coherence BW)
Doppler spread defines maximum nonzero doppler, its inverse is coherence time
  Channel decorrelates over channel coherence time