## Slide 1: Time Traveling Hardware and Software Systems
Xiangyao Yu, Srini Devadas
CSAIL, MIT
Notes: Good afternoon.
Great pleasure to be here to share my research with you.
My name…
I’m a computer system guy, interested in both … and I will talk about both.
In this presentation, I’m going to talk about a new concept of time that we recently invented.
It is able to improve the scalability of shared memory systems that have consistency requirement.

## Slide 2: For Fifty years, we have ridden Moore’s Law
Moore’s Law and the scaling of clock frequency = printing press for the currency of performance
Notes: Wait a few months, and performance improves...

## Slide 3: Technology Scaling
Chart: 
Frequency (MHz) | 0.7 | 0.5 | 2 | 5 | 6 | 16 | 16 | 40 | 25 | 33 | 66 | 100 | 60 | 200 | 40 | 66 | 300 | 150 | 300 | 90 | 200 | 200 | 200 | 200 | 90 | 500 | 250 | 533 | 233 | 300 | 500 | 400 | 300 | 450 | 500 | 750 | 1000 | 1000 | 900 | 2000 | 800 | 1400 | 2200 | 1800 | 1000 | 1150 | 2160 | 1800
Power (W) | 0.45 | 0.42 | 0.92 | 1.7 | 3 | 1.5 | 3 | 4 | 2.75 | 3.5 | 5.8 | 15 | 14.2 | 35 | 3 | 13 | 28 | 3 | 50 | 16 | 32.6 | 30 | 10 | 30 | 11 | 43 | 25 | 36 | 17 | 32 | 91 | 14 | 30 | 17 | 21 | 35 | 49 | 20 | 70 | 72 | 98 | 56 | 48 | 62 | 98 | 155 | 74 | 89
Cores | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1800 | 2600 | 1900 | 3600 | 3200 | 2800 | 1200 | 2200 | 2600 | 3600 | 2800 | 2660 | 2800 | 2330 | 2930 | 4700 | 4000 | 2000 | 1400 | 2000 | 2300 | 3000 | 2500 | 3200 | 2660 | 3200 | 2300 | 3500 | 2266 | 1660 | 2400 | 3330 | 3000 | 3600
 | 89 | 89 | 100 | 115 | 130 | 85 | 72 | 25 | 65 | 130 | 125 | 65 | 75 | 31 | 130 | 100 | 100 | 31 | 84 | 75 | 95 | 65 | 95 | 130 | 130 | 130 | 250 | 200 | 130 | 139 | 130 | 130 | 139 | 125
 | 1 | 1 | 2 | 1 | 2 | 1 | 8 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 2 | 9 | 2 | 8 | 4 | 4 | 2 | 3 | 4 | 6 | 8 | 16 | 8 | 8 | 16 | 10 | 6 | 8 | 8
Transistors x 1000
Clock frequency (MHz)
Power (W)
Cores
Each generation of Moore’s law doubles the number of transistors but clock frequency has stopped increasing.

## Slide 4: Technology Scaling
Chart: 
Frequency (MHz) | 0.7 | 0.5 | 2 | 5 | 6 | 16 | 16 | 40 | 25 | 33 | 66 | 100 | 60 | 200 | 40 | 66 | 300 | 150 | 300 | 90 | 200 | 200 | 200 | 200 | 90 | 500 | 250 | 533 | 233 | 300 | 500 | 400 | 300 | 450 | 500 | 750 | 1000 | 1000 | 900 | 2000 | 800 | 1400 | 2200 | 1800 | 1000 | 1150 | 2160 | 1800
Power (W) | 0.45 | 0.42 | 0.92 | 1.7 | 3 | 1.5 | 3 | 4 | 2.75 | 3.5 | 5.8 | 15 | 14.2 | 35 | 3 | 13 | 28 | 3 | 50 | 16 | 32.6 | 30 | 10 | 30 | 11 | 43 | 25 | 36 | 17 | 32 | 91 | 14 | 30 | 17 | 21 | 35 | 49 | 20 | 70 | 72 | 98 | 56 | 48 | 62 | 98 | 155 | 74 | 89
Cores | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 1800 | 2600 | 1900 | 3600 | 3200 | 2800 | 1200 | 2200 | 2600 | 3600 | 2800 | 2660 | 2800 | 2330 | 2930 | 4700 | 4000 | 2000 | 1400 | 2000 | 2300 | 3000 | 2500 | 3200 | 2660 | 3200 | 2300 | 3500 | 2266 | 1660 | 2400 | 3330 | 3000 | 3600
 | 89 | 89 | 100 | 115 | 130 | 85 | 72 | 25 | 65 | 130 | 125 | 65 | 75 | 31 | 130 | 100 | 100 | 31 | 84 | 75 | 95 | 65 | 95 | 130 | 130 | 130 | 250 | 200 | 130 | 139 | 130 | 130 | 139 | 125
 | 1 | 1 | 2 | 1 | 2 | 1 | 8 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 2 | 9 | 2 | 8 | 4 | 4 | 2 | 3 | 4 | 6 | 8 | 16 | 8 | 8 | 16 | 10 | 6 | 8 | 8
Transistors x 1000
Clock frequency (MHz)
Power (W)
Cores
To increase performance, need to exploit parallelism.

## Slide 5: Different Kinds of Parallelism - 1
Instruction Level
a = b + c
d = e + f
g = d + b
Transaction Level
Read A
Read B
Compute C
Read A
Read D
Compute E
Read C
Read E
Compute F
Notes: Transactions need to be atomically executed, but otherwise can run in parallel.

## Slide 6: Different Kinds of Parallelism - 2
Thread Level
A
B
C
x
=
Different thread computes each entry of product matrix C
Task Level
Cloud
Search(“image”)

## Slide 7: Different Kinds of Parallelism - 3
Thread Level
A
B
C
x
=
Different thread computes each entry of product matrix C
User Level
Cloud
Search(“image”)
Query(“record”)
Lookup(“data”)
Notes: User Level or Embarrassing Level

## Slide 8: Dependency Destroys Parallelism
for i = 1 to n
a[b[i]] = (a[b[i - 1]] + b[i]) / c[i]
Need to compute ith entry after i - 1th has been computed 

## Slide 9: Different Kinds of Dependency
Write A
Read A
RAW:
Read needs
new value
Write A
Write A
WAW:
Semantics
decide
order
Read A
Write A
WAR:
We have
flexibility
here!
No dependency!
Read A
Read A

## Slide 10: Dependence is Across Time, But What Is Time?
Time can be physical time
Time could correspond to logical timestamps assigned to instructions
Time could be a combination of the above
 Time is a definition of ordering

## Slide 11: WAR Dependence
Read A
Read happens later than Write in physical time but is before Write in logical time.
Write A
Thread 0
Thread 1
Logical
Order
Initially A = 10
A=13
Local copy of A = 10
Physical Time
Order

## Slide 12: What Is Correctness?
We define correctness of a parallel program based on its outputs in relation to the program run sequentially

## Slide 13: SEQUENTIAL CONSISTENCY
A B
C D
Global Memory Order
A B C D
A C B D
C D A B
C B A D
Can we exploit this freedom in correct execution to avoid dependency?

## Slide 14: Avoiding Dependency Across the Stack
Circuit
Efficient atomic instructions
Multicore
Processor
Multicore
Database
Distributed
Database
Distributed
Shared Memory
Tardis coherence protocol
TicToc concurrency control
with Andy Pavlo and Daniel Sanchez
Distributed TicToc
Transaction processing with fault tolerance
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 15: Shared Memory Systems
Multi-core Processor
OLTP Database
Cache Coherence
Concurrency Control
Notes: shared memory is increasing important and popular. example: mutli-core, dbms, dsm, etc.
Consistency is a challenge
Cache coherence and concurrency control

## Slide 16: Directory-Based Coherence
Data replicated and cached locally for access
Uncached data copied to local cache, writes invalidate data copies
P
P
P
P
P
P
P
P
P

## Slide 17: Cache Coherence Scalability
Read A
Read A
Write A
Invalidation
O(N) Sharer List
Chart: Core Count
| 16.0 | 64.0 | 256.0 | 1024.0
Directory | 0.03125 | 0.125 | 0.5 | 2
Today

## Slide 18: Lease-Based Coherence
Time
t=0
1
2
3
4
5
6
7
Ld(A)
A read gets a lease on a cacheline
Lease renewal after lease expires
A store can only commit after leases expire
Tardis: logical leases
Core 0
Core 1
St(A)
Logical
Timestamp
Ld(A)
Write Timestamp
(wts)
Read
Timestamp
(rts)
Program
Timestamp
(pts)
Ld(A)
Notes: Logical timestamp is managed at a per-core basis similar to Lamport clock.
The timestamp of different cores can move at different pace.
At the same physical time, different cores can be at different logical time.
Cores synchronize their logical timestamps only when there is data dependency between threads.
Using logical time instead of physical time significantly improves the performance and scalability of Tardis.
- no need for globally synchronized clocks.
- a store does not wait in physical time.

## Slide 19: Logical Timestamp
logical time
Invalidation
Physical Time Order
Logical Time Order
(concept borrowed from database)
Old Version
New Version
Tardis
(No Invalidation)
Notes: Invalidation is due to physical time: later reads should observe the current write. But physical time is too strict.
In Tardis, we use physiological time. and use timestamps to do explicit version control.
For write, just create a new version.
co-exist at P time, but separate in L time. And still consistent.

## Slide 20: Timestamp Management
Core
pts=5
Shared LLC
wts
rts
A
Cache
B
A
S
0
10
S
0
10
S
0
5
state
Program Timestamp (pts)
Timestamp of last memory operation
Write Timestamp (wts)
Data created at wts
Read Timestamp (rts)
Data valid from wts to rts
Logical Time
wts
rts
Lease
Notes: explain pts, wts and rts.
----- Meeting Notes (1/31/16 11:26) -----
!!!!!!!!!
timestamps only on chip. Not in main memory.!!!
!!!!!!!!!!

## Slide 21: Two-Core Example
Core 0
Cache
pts=0
A
S
0
0
B
S
0
0
Core 1
Cache
pts=0
physical
time
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5

## Slide 22: Store A @ Core 0
Core 0
pts=0
A
S
0
0
B
S
0
0
Core 1
pts=0
Write at pts = 1
ST(A) Req
M
0
0
A
M
1
1
M
owner:0
pts=1
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5

## Slide 23: Load B @ Core 0
Core 0
pts=1
A
M
B
S
0
0
Core 1
pts=0
A
M
1
1
owner:0
LD(B) Req
S
0
11
S
0
11
B
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5
Reserve rts to pts + lease = 11

## Slide 24: Store B @ Core 1
Core 0
pts=1
A
M
B
S
0
11
Core 1
pts=0
A
M
1
1
owner:0
B
S
0
11
ST(B) Req
M
owner:1
M
0
11
M
12
12
pts=12
B
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5
Exclusive ownership returned
No invalidation

## Slide 25: Two Versions Coexist
Core 0
pts=1
A
M
B
Core 1
A
M
1
1
owner:0
B
S
0
11
M
owner:1
M
12
12
pts=12
B
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5
Core 1 traveled ahead in time
Versions ordered in logical time

## Slide 26: Load A @ Core 1
Core 0
pts=1
A
M
B
Core 1
A
M
1
1
owner:0
B
S
0
11
Write back request to Core 0
Downgrade from M to S
Reserve rts to pts + lease = 22
M
owner:1
M
12
12
pts=12
B
LD(A) Req
WB(A) Req
S
1
22
S
1
22
S
1
22
A
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5

## Slide 27: Load B @ Core 0
Core 0
pts=1
A
M
Core 1
pts=12
A
owner:0
B
S
0
11
B
M
owner:1
B
M
12
12
> , <
physical time
logical timestamp
S
1
22
S
1
22
A
Cache
Cache
Core 0
store A
load B
load B
Core 1
store B
load A
1
2
3
4
5
physical
time
5
4
logical
time
5
4
global memory order ≠ physical time order

## Slide 28: Summary of Example
Core 1
store B
load A
Core 0
store A
load B
load B
Tardis
physical
time
Directory
Core 1
store B
load A
Core 0
store A
load B
load B
WAR
RAW
physical + logical time order
physical time order
RAW
RAW
WAR
Notes: In this slide, we compare the directory coherence protocol with Tardis on the example I have shown.
The y axis here is the physical time order and the blue arrows indicate the sequential order.
emphasize 3 vs. 1
----- Meeting Notes (1/31/16 11:26) -----
explain the conflicts for the first time.
explain why WAR for Tardis is green.

## Slide 29: Physiological Time
Global Memory Order
Core 1
store B (12)
load A (12)
Core 0
store A (1)
load B (1)
load B (1)
Tardis
X <PL Y := X <L Y or (X =L Y and X <P Y)
Physical Time
Logical Time
Physiological Time
1
2
3
Thm: Tardis obeys Sequential Consistency

## Slide 30: Tardis Pros and Cons
Scalability
No Invalidation, Multicast or Broadcast
Lease Renew
Speculative Read
Timestamp Size
Timestamp Compression
Time Stands Still
Livelock Avoidance

## Slide 31: Evaluation
Storage overhead per cacheline (N cores)
Directory: N bits per cacheline
Tardis: Max(Const, log(N)) bits per cacheline
Chart: 
| 16.0 | 64.0 | 256.0 | 1024.0
Directory | 0.03125 | 0.125 | 0.5 | 2
Tardis | 0.078125 | 0.078125 | 0.078125 | 0.078125
Notes: 7.8%

## Slide 32: Speedup
Graphite Multi-core Simulator (64 cores)
Chart: Normalized Speedup
| FMM | BARNES | CHOLESKY | VOLREND | OCEAN-C | OCEAN-NC | FFT | RADIX | LU-C | LU-NC | WATER-NSQ | WATER-SP | CANNEAL | STREAMCLUS. | SWAPTIONS | BLACKSCH. | SPMV | SYMGS | YCSB | TPCC | AVG
DIRECTORY | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
TARDIS | 1.0072 | 1.0041 | 0.9964 | 1.0015 | 1.0392 | 1.0414 | 1.0051 | 1.0046 | 1.0022 | 1.0067 | 1.0032 | 1.0033 | 1.0093 | 1.0619 | 1.0001 | 1.0001 | 1.018 | 0.98563 | 1.0147 | 1.0056 | 1.0105
TARDIS AT 256 CORES | 0.97509 | 1.0276 | 0.99961 | 0.99978 | 1.0992 | 1.1078 | 1.0977 | 1.0579 | 1.0696 | 0.98237 | 1.0441 | 1.0073 | 1.0062 | 1.2129 | 1.0001 | 1.0001 | 1.0087 | 0.96537 | 1.0046 | 1.0161 | 1.0341
Notes: Graphite simulator

## Slide 33: Network Traffic
Chart: Normalized Traffic
| FMM | BARNES | CHOLESKY | VOLREND | OCEAN-C | OCEAN-NC | FFT | RADIX | LU-C | LU-NC | WATER-NSQ | WATER-SP | CANNEAL | STREAMCLUS. | SWAPTIONS | BLACKSCH. | SPMV | SYMGS | YCSB | TPCC | AVG
DIRECTORY | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
TARDIS | 0.97958 | 0.89288 | 0.9814 | 1.0264 | 0.93875 | 0.92699 | 0.9652 | 0.97601 | 0.94376 | 0.95994 | 0.87113 | 0.929 | 0.99409 | 0.84092 | 0.94208 | 0.89114 | 0.90686 | 0.94703 | 0.95826 | 1.0194 | 0.94454
TARDIS AT 256 CORES | 0.99822 | 0.88975 | 0.97927 | 0.99602 | 0.94739 | 0.92184 | 0.94423 | 0.9762 | 0.92916 | 0.95155 | 0.85757 | 0.9257 | 0.97478 | 0.83627 | 0.94311 | 0.88611 | 0.9063 | 0.94317 | 0.959 | 1.0085 | 0.9387

## Slide 34
Snoopy Coherence
Directory Coherence
Optimized Directory
TARDIS
Storage
Overhead
Performance
Degradation
High
Complexity
Network
Traffic

## Slide 35: Concurrency Control
Serializability
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
Results should correspond to some serial order of atomic execution
Notes: TODO. mention the 1000 core work here.
Use the 1000 core graph

## Slide 36: Concurrency Control
Can’t Have This
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
BEGIN
COMMIT
Results should correspond to some serial order of atomic execution
Notes: TODO. mention the 1000 core work here.
Use the 1000 core graph

## Slide 37: Bottleneck 1: Timestamp Allocation
Centralized Allocator
  Timestamp allocation is a scalability bottleneck
Synchronized Clock
  Clock skew causes unnecessary aborts
Chart: Thread Count
| 1.0 | 4.0 | 10.0 | 20.0 | 40.0 | 60.0 | 80.0
T/O | 0.50639 | 1.5776 | 2.8891 | 2.4056 | 2.1033 | 3.2105 | 4.1332
2PL | 0.51151 | 1.6169 | 4.0607 | 7.9034 | 14.8068 | 18.131 | 20.8482
Notes: Title: T/O bottlenecks/challenges
Use the conclusion as the title.
For example, many algorithms use TS.
TS is unique and monotonically increases
Txn with larger TS should observe updates made by Txn with smaller TS. But not the other way around.
Two common approaches: TS allocation and synchronized clock.
Neither is scalable:
Another downside: static allocation independent of data access pattern. This causes unnecessary aborts.
First txn does not observe the update made by the second txn. So it must be ordered before txn2 in the global serial order.
So if TS1 > TS2 commit, else abort.

## Slide 38: Bottleneck 2: Static Assignment
T1@ts=1
Timestamps assigned before a transaction starts
Suboptimal assignment leads to unnecessary aborts.
T2@ts=2
BEGIN
COMMIT
READ(A)
BEGIN
COMMIT
WRITE(A)
T1@ts=2
T2@ts=1
BEGIN
COMMIT
READ(A)
BEGIN
ABORT
WRITE(A)
Time
Notes: For example, many algorithms use TS.
TS is unique and monotonically increases
Txn with larger TS should observe updates made by Txn with smaller TS. But not the other way around.
Two common approaches: TS allocation and synchronized clock.
Neither is scalable:
Another downside: static allocation independent of data access pattern. This causes unnecessary aborts.
First txn does not observe the update made by the second txn. So it must be ordered before txn2 in the global serial order.
So if TS1 > TS2 commit, else abort.

## Slide 39: Key Idea: Data Driven Timestamp Management
Traditional T/O
Acquire timestamp (TS)
Determine tuple visibility using TS
TicToc
Access tuples and remember their timestamp info.
Compute commit timestamp (CommitTS)
No Timestamp Allocation
Dynamic Timestamp Assignment
Timestamp Allocation
Static Timestamp Assignment

## Slide 40
Data
wts
(Write Timestamp)
rts
(Read Timestamp)
Tuple Format
BEGIN
COMMIT
READ
PHASE
VALIDATION
PHASE
WRITE
PHASE
Read & Write Tuples
Execute Transaction
Compute CommitTS
Decide Commit/Abort
Update Database
TicToc Transaction Execution
wts : last data write @ wts
rts : last data read @ rts
data valid between wts and rts

## Slide 41
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
TicToc Example
T1
T2
v1
v1
Database States
Transaction Local States
Tuple A
Tuple B

## Slide 42
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Load A from T1
T1
T2
v1
v1
Tuple A
Tuple B
Load a snapshot of tuple A
  Data, wts and rts
Notes: For a load operation, make a local copy of data and timestamps (taking a snapshot)

## Slide 43
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Load A from T2
T1
T2
v1
v1
Tuple A
Tuple B
Load a snapshot of tuple A
  Data, wts and rts

## Slide 44
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Store B from T1
T1
T2
v1
v1
Tuple A
Tuple B
Store B to local write set
Notes: A store is performed to the local write set, not visible to the rest of the system yet.
Here we assume a store is always an update. Namely, the txn always loads B before storing to it.

## Slide 45
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Load B from T2
T1
T2
v1
v1
Tuple A
Tuple B
Load a snapshot of tuple B
  Data, wts and rts

## Slide 46
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Commit Phase of T1
T1
T2
v1
v1
Tuple A
Tuple B
Compute CommitTS
Write Set:
tuple.rts+1 ≤ CommitTs
Read Set:
tuple.wts ≤ CommitTs ≤ tuple.rts

## Slide 47
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Commit Phase of T1
T1
T2
v1
v1
Tuple A
Tuple B
rts extension on tuple A
T1 commits
@ TS=2

## Slide 48
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Commit Phase of T1
T1
T2
v1
v1
Tuple A
Tuple B
Copy tuple B from write set to database
v2
T1 commits
@ TS=2

## Slide 49
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Commit Phase of T2
T1
T2
v1
v1
Tuple A
Tuple B
Compute CommitTS for T2
Find consistent read time for T2 (no writes in T2)
v2
T1 commits
@ TS=2
Notes: T2 is readonly, it needs a commit timestamp at which it can observe a consistent view of both tuples.
The commit timestamp of T2 can be either TS=0 or TS=1. We pick 0 since it is small.

## Slide 50
Logical Time
Transaction 1
load A
store B
commit?
Transaction 2
load A
load B
commit?
1
3
5
2
4
6
0
1
2
3
4
Final State
T1
T2
v1
v1
Tuple A
Tuple B
v2
T1 commits
@ TS=2
T2 commits
@ TS=0
Txn 1 < Txn 2
Txn 2 < Txn 1
physical
time
logical
time
Notes: Interesting facts:
T2 can commit even if A has been updated.
T2 starts later than T1, and commits later than T1, but T2 is ordered logically before T1.

## Slide 51: Experimental Setup
DBx1000: Main Memory DBMS
  No logging
  No B-tree (hash indexing)
Concurrency Control Algorithms
  MVCC: HEKATON (Microsoft)
  OCC: SILO (Harvard/MIT)
  2PL: DL_DETECT, NO_WAIT
10 GB YCSB Benchmark
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 52: Evaluation
YCSB -- Medium Contention
YCSB -- High Contention
Chart: Thread Count
| 1.0 | 4.0 | 10.0 | 20.0 | 40.0 | 60.0 | 80.0
TICTOC | 0.09382 | 0.30167 | 0.75441 | 1.4473 | 2.5709 | 3.2574 | 3.7036
HEKATON | 0.071792 | 0.24981 | 0.57232 | 1.0338 | 1.5661 | 1.6488 | 1.7037
DL_DETECT | 0.077722 | 0.24236 | 0.5902 | 1.0657 | 0.43411
NO_WAIT | 0.078531 | 0.25881 | 0.60108 | 1.1328 | 0.62595 | 0.3501 | 0.26012
SILO | 0.098652 | 0.32099 | 0.78941 | 1.4974 | 2.3197 | 3.2529 | 3.8657
Chart: Thread Count
| 1.0 | 4.0 | 10.0 | 20.0 | 40.0 | 60.0 | 80.0
TICTOC | 0.10485 | 0.27623 | 0.51158 | 0.69947 | 0.82114 | 0.83088 | 0.81366
HEKATON | 0.062094 | 0.19813 | 0.25416 | 0.23926 | 0.20451 | 0.19982 | 0.20385
DL_DETECT | 0.077331 | 0.081499 | 0.062599 | 0.030991 | 0.0047059 | 0 | 0
NO_WAIT | 0.088819 | 0.27974 | 0.30398 | 0.315 | 0.29817 | 0.2744 | 0.24741
SILO | 0.10927 | 0.27492 | 0.44128 | 0.54178 | 0.51514 | 0.47499 | 0.42356
Chart: 
| 1.0 | 4.0 | 10.0 | 20.0 | 40.0 | 60.0 | 80.0
TICTOC | 0.09382 | 0.30167 | 0.75441 | 1.4473 | 2.5709 | 3.2574 | 3.7036
HEKATON | 0.071792 | 0.24981 | 0.57232 | 1.0338 | 1.5661 | 1.6488 | 1.7037
DL_DETECT | 0.077722 | 0.24236 | 0.5902 | 1.0657 | 0.43411
NO_WAIT | 0.078531 | 0.25881 | 0.60108 | 1.1328 | 0.62595 | 0.3501 | 0.26012
SILO | 0.098652 | 0.32099 | 0.78941 | 1.4974 | 2.3197 | 3.2529 | 3.8657

## Slide 53: TicToc Discussion
Transactions may have same CommitTS
Logical timestamp growing rate indicates inherent parallelism
Chart: # of Committed Txns
Thm: Serializability = All ops valid at CommitTS
Notes: TODO
different txns have the same TS
inherent parallelism in transactions depends on max TS

## Slide 54: Physiological Time Across the Stack
Circuit
Efficient atomic instructions
Multicore
Processor
Multicore
Database
Distributed
Database
Distributed
Shared Memory
Tardis coherence protocol
TicToc concurrency control
Distributed TicToc
Transaction processing with fault tolerance
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 55: Atomic Instruction (LR/SC)
ABA Problem
Detect ABA using timestamp (wts)
Core 0
Core 0
LR(x); # x = A
ST(x); # x = B
ST(x); # x = A
SC(x); # x = A
ABA?
Notes: ABA problem can manifest itself in many different contexts. I illustrate how it can be resolved in load reserve/store conditional (LR/SC) instructions using logical timestamps. The SC is supposed to update the cacheline if it has not been changed since LR. One naive solution is to check the value of the cacheline before doing SC, and only update if the value is the same as observed by the previous LR. But this solution has ABA problem. It may be the case that when C0 LR cacheline x, it observes value A. Then, a different core C1 updates x and later update x again back to the original value (x = A). Now if C0 does SC, it will see that the value of x is the same as observed by the previous LR. Therefore, SC will commit according to the naive solution. But in fact, the value has been changed since the last LR, and thus the SC should not commit… Tardis can solve this problem using logical timestamps. The wts of each cacheline indicates the version of the line. A LR remembers the wts, and SC checks if the wts has been changed. If they are the same, then the cacheline must be the same one observed by the previous LR (writes by different cores always increment the wts). ABA is no longer a problem :-) Actually, by checking the wts, Tardis is more efficient as it dose not check the value. For today’s systems that don’t have Tardis, the ABA problem can be avoided by failing the SC if the cacheline has ever been invalidated from the private cache. For the example above, this can avoid the ABA problem. But this solution is not perfect. If the LR line is ever evicted/invalidated from the private cache, then the LR/SC will always fail. In some systems (e..g, RISC-V), livelock can actually occur. Here is how livelock may happen in RISCV. In RISCV, a LR always loads the cacheline in Exclusive or Modified state. We may have two cores, both LR/SC on the same cacheline. C0 does LR. Then C1 does LR, invalidating C0’s copy, so C0 fails. C0 retires and does LR again, invalidating C1’s copy, so C1 fails. … RICSV has a ‘hack’ to resolve this by keeping a line in E/M state for at least 32 cycles after the LR. So if the SC comes within 32 cycles, it will always succeed. But this hack does not work if the SC comes more than 32 cycles after the LR.

## Slide 56: Tardis Cache Coherence
Simple: No Invalidation
Scalable:
  O(log N) storage
  No Broadcast, No Multicast
  No Clock Synchronization
Support Relaxed Consistency Models
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 57: T1000: Proposed 1000-Core Shared Memory Processor

## Slide 58: TicToc Concurrency Control
Data Driven Timestamp Management
No Central Timestamp Allocation
Dynamic Timestamp Assignment
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 59: Distributed TicToc
Data Driven Timestamp Management
Efficient Two-Phase Commit Protocol
Support Local Caching of Remote Data
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 60: Fault Tolerant Distributed Shared Memory
Transactional Programming Model
Distributed Command Logging
Dynamic Dependency Tracking Among Transactions (WAR dependency can be ignored)
Notes: No logging, hash index (no btree)
----- Meeting Notes (1/31/16 11:43) -----
Say I implemented DBx1000, used for 1000 core paper.
It works for Graphite simulator and it also runs alone.
introduce DBx1000. plugable CC algos.
HEKATON -> MS hekaton
silo MIT/Harvard Silo

## Slide 61: Time Traveling to Eliminate WAR
Xiangyao Yu, Srini Devadas
CSAIL, MIT