## Slide 1: Diffusion Tensor Imaging
White matter measurements
Diffusion weighted imaging
Tractography
Statistics
Tests of the validity and examples

## Slide 2: White matter connections: long-range

## Slide 3: White matter damage is common
Figure 2
Figure 1
Pediatric Neurology Volume 30, Issue 2 , February 2004, Pages 140-142
Notes: Figure 1. Preoperative T2-weighted (TR/TE: 6000/99) magnetic resonance imaging scan of the brain, revealing an exophytic mass (5.5 × 3.8 cm) centered in the left thalamus, extending into the posterior left temporal lobe and left aspect of the midbrain, causing mass effect.
Figure 2. Postoperative T2-weighted (TR/TE: 6000/99) magnetic resonance imaging scan of the brain, depicting the exophytic mass and hemorrhage in the surgical bed. The ventricles have been slightly decompressed after a ventriculostomy (not observed in this view). The white arrow and cross refer to the inability of visual information from the right occipital lobe to reach the angular gyrus and language areas in the left hemisphere, owing to the disruption of the forceps major and splenium of the corpus callosum.
Alexia without agraphia following biopsy of a left thalamic tumor
Madhura A. Tamhankar MD , †, Harry B. Coslett MD †, Michael J. Fisher MD ‡, Leslie N. Sutton MD § and Grant T. Liu MD , , † * Neuro-ophthalmology, The Children's Hospital of Philadelphia, Philadelphia, Pennsylvania, USA ‡ Neuro-oncology, The Children's Hospital of Philadelphia, Philadelphia, Pennsylvania, USA § Neurosurgery services, The Children's Hospital of Philadelphia, Philadelphia, Pennsylvania, USA † Department of Neurology, Hospital of the University of Pennsylvania, University of Pennsylvania School of Medicine;, Philadelphia, Pennsylvania, USA Received 18 February 2003; accepted 2 July 2003. Available online 6 January 2004.

## Slide 4: White matter deficits can be specific: Acquired alexia from a callosal lesion
Figure 1 from Mao-Draayer & Panitch (2004), Alexia without agraphia in multiple schlerosis...
L
R
Notes: Figure 1 Axial and sagittal fluid attenuation inversion recovery (FLAIR) MRI demonstrates lesions in the splenium of the corpus callosum (A and B) and the left occipital WM adjacent to the occipital horn of the lateral ventricle (C).
Alexia without agraphia in multiple sclerosis: case report with magnetic resonance imaging localization
Yang Mao-Draayer and Hillel Panitch
Department of Neurology, University of Vermont College of Medicine, Burlington, VT, USA
Multiple Sclerosis (2004) 10, 705 /707
The syndrome of alexia without agraphia occurs rarely in multiple sclerosis (MS). We report a patient with right homonymous hemianopsia and alexia without agraphia as his initial manifestations of relapsing / remitting MS. Magnetic resonance imaging (MRI) demonstrated a hyperintense lesion in the left occipital subcortical white matter (WM) and an enhancing lesion in the splenium of the corpus callosum. The clinical presentation and MRI findings were consistent with disconnection of the functional right occipital visual cortex from structures responsible for language comprehension in the left hemisphere. The diagnosis of MS was confirmed by subsequent development of additional periventricular WM lesions.

## Slide 5: White Matter Development: Cortical Folding (van Essen)
Van Essen (Nature 1997) A tension-based theory of morphogenesis and compact wiring in the central nervous system.
Neurons migrate to the cortical plate and begin to grow axons
Axons create mechanical tension that draws connected region closer

## Slide 6: White Matter Development: Cortical Folding (van Essen)
Van Essen (Nature 1997) A tension-based theory of morphogenesis and compact wiring in the central nervous system.
Neurons migrate to the cortical plate and begin to grow axons
Axons create mechanical tension that draws connected region closer
Gyri group strongly interconnected regions, sulci separate weakly interconnected regions
Cortical folding causes shearing

## Slide 7: Oligodendrocytes and axon caliber

## Slide 8: Axon size and myelin thickness (rat cervical ventral spinal nerve roots, Fraher, 1972)
Axon perimeter size
Myelin thickness (lamellae)
P18
Notes: Fig. 3. Scatterplots relating myelin sheath thickness to axon perimeter at P18 for (a) the observed population, derived from Fraher (1972) and (b) the hypothetical population. Note the close similarity of the scatterplots. A well de®ned secondary cluster of points (representing gamma ®bres) is present at the lower left of the observed plot (see text).

## Slide 9: Axon size and myelination determine neural conduction speed
myelinated
unmyelinated

## Slide 10: White matter development
Age (years)
Overall volume set around 12-15

## Slide 11: Diffusing Water Probes Microscopic Tissue Structure
Tissue structures affect diffusion
MR diffusion measures depend on microscopic structure within voxel
Diffusion through white matter probes:
  density of axons
  degree of myelination
  average fiber diameter
  directional similarity of axons

## Slide 12: 5.17 Diffusion. Over time, molecules within gases or liquids will move freely through the medium.
Notes: fmri-fig-05-17-0.jpg

## Slide 13: 5.18 Isotropic and anisotropic diffusion.
Notes: fmri-fig-05-18-0.jpg

## Slide 14: Bloch-Torrey Equations
Alexander Hopf

## Slide 15: Bloch-Torrey Equations
Alexander Hopf

## Slide 16: Diffusion coefficient
Magnetization depends on diffusion. This is beyond the stuff I taught earlier (Bloch equations).
When we add diffusion, it is called Bloch-Torry.
It turns out that diffusion disturbs the T2 images
Diffusion coefficient
Sequence-dependent constant

## Slide 17: Stejskal-Tanner Equation (NMR)‏
Signal attenuation = exp(-b * ADC)‏

## Slide 18: DTI: How it works
Bipolar gradient pulse (“diffusion-weighting”)
  Pulse pair has no net effect on stationary spins
    Second pulse undoes first
  Spins moving along gradient are not rephased by second pulse and end up phase-shifted
    Phase-shift  distance moved during time T
RF
acquisition
Gradient
t
G
Notes: Imagine a single spinning proton. In the presence of a gradient field G1, it will spin at a slightly higher rate than its larmour frequency and so its spin phase (relative to its neighbours) will change over time. The final amount of phase shift will be proportional to the local value of the field and the amount of time that the graident is applied. Now if you reverse the gradient for the same amount of time, (G2) you should undo the phase shift and the proton will be spinning in the same phase that it started in.
But - now if the proton has some translational movement, it will be in
different places during G1 and G2. It will experience different magnetic
fields during the two periods and at the end, there will be some
residual phase shift. You can detect this phase shift with MR (in fact,
in standard MR, motion and flow artefacts are a big problem that people
spend a lot of time trying to get rid of). Note that this only happens
if the proton moves up or down the gradient (so changing it's local
field strength between G1 and G2). So you are tuned to detect motion in
a particular direction.
By changing the physical direction of G1/G2, you can tune your sequence to detect motion in different directions. DTI sequences typically pick 6 directions and regenerate the diffusion tensor from the diffusion-weighted images obtained.

## Slide 19: Diffusion-weighted gradient echo sequence (Stejskal-Tanner)
  Gradient pair (G,-G) has no net effect on stationary spin
  Second pulse undoes first
  Moving spins are not re-phased by second pulse
  Phase-shift causes a signal decay that depends on the distance moved during time DT (diffusion time)
Functional Magnetic Resonance Imaging (2004). Huettel et al., Fig 5.19B

Notes: Imagine a single spinning proton. In the presence of a gradient field G1, it will spin at a slightly higher rate than its larmour frequency and so its spin phase (relative to its neighbours) will change over time. The final amount of phase shift will be proportional to the local value of the field and the amount of time that the graident is applied. Now if you reverse the gradient for the same amount of time, (G2) you should undo the phase shift and the proton will be spinning in the same phase that it started in.
But - now if the proton has some translational movement, it will be in
different places during G1 and G2. It will experience different magnetic
fields during the two periods and at the end, there will be some
residual phase shift. You can detect this phase shift with MR (in fact,
in standard MR, motion and flow artefacts are a big problem that people
spend a lot of time trying to get rid of). Note that this only happens
if the proton moves up or down the gradient (so changing it's local
field strength between G1 and G2). So you are tuned to detect motion in
a particular direction.
By changing the physical direction of G1/G2, you can tune your sequence to detect motion in different directions. DTI sequences typically pick 6 directions and regenerate the diffusion tensor from the diffusion-weighted images obtained.

## Slide 20: Protons Precessing in Phase
Notes: Apply two large field gradient pulses between excitation of spins and signal acquisition
Second pulse “undoes” effects of first for stationary spins
Spins that moved between pulses are not completely rephased and thus produce weaker signals

## Slide 21: Diffusion Weighting: First Pulse
Gradient over space

## Slide 22: Time to Diffuse

## Slide 23: Diffusion Weighting: Second Pulse
Gradient over space

## Slide 24: Reduced signal from spin dephasing
Stejskal-Tanner equation:
Signal attenuation = exp(-b * ADC)

## Slide 25: 5.19 Pulse sequences used for diffusion-weighted imaging.
Notes: fmri-fig-05-19-0.jpg

## Slide 26: 5.19 Pulse sequences used for diffusion-weighted imaging.
Notes: fmri-fig-05-19-0.jpg

## Slide 27
GET SLIDE SEQUENCE FROM UTILITY SLIDES

## Slide 28: Raw Diffusion MR Images
b = 0
No diffusion weighting- the reference image

## Slide 29: Raw Diffusion MR Images
b = 0
Dark means large ADC (a great deal of signal attenuation)

## Slide 30: Raw Diffusion MR Images
b = 800
g = [-0.7 0.7 0.0]
Dark means large ADC (a great deal of signal attenuation)

## Slide 31: Raw Diffusion MR Images
b = 800
g = [-0.7 -0.7 0.0]
Dark means large ADC (a great deal of signal attenuation)

## Slide 32: Computing the ADC image in a direction

## Slide 33: Apparent diffusion coefficient (A)
Sd
S0
0
1
2
3
4
A
um2/ms
a.u.
g = (-0.7 0.7 0.0)
Direction

## Slide 34: ADC Image
g = (-0.7 0.7 0.0)
Brighter means more diffusion in the gradient direction

## Slide 35: Diffusion Numbers
In 1 ms, a water molecule will be, on average, 1um from its starting point.

## Slide 36: Diffusion Tensor Imaging
Short version:
Measure in multiple directions and summarize iso-diffusion surface as an ellipsoid
Notes: They used pork loin for a sample. Also excised slice of a cat brain. But, really, pork loin?
Mosley argued that one could see fiber orientation even in his initial paper.
See also the related paper in which they start to understand the tensor and its measurement
Estimation of the effective self-diffusion tensor from the NMR spin echo.
Basser PJ,
Mattiello J,
LeBihan D.
Biomedical Engineering and Instrumentation Program, Warren G. Magnuson Clinical Center, National Institutes of Health, Bethesda, Maryland 20892.
The diagonal and off-diagonal elements of the effective self-diffusion tensor, Deff, are related to the echo intensity in an NMR spin-echo experiment. This relationship is used to design experiments from which Deff is estimated. This estimate is validated using isotropic and anisotropic media, i.e., water and skeletal muscle. It is shown that significant errors are made in diffusion NMR spectroscopy and imaging of anisotropic skeletal muscle when off-diagonal elements of Deff are ignored, most notably the loss of information needed to determine fiber orientation. Estimation of Deff provides the theoretical basis for a new MRI modality, diffusion tensor imaging, which provides information about tissue microstructure and its physiologic state not contained in scalar quantities such as T1, T2, proton density, or the scalar apparent diffusion constant.

## Slide 37: The Diffusion Tensor is a Model of Anisotropic Gaussian Diffusion
3x3 symmetric matrix Q
Diffusion iso-probability contour describes an ellipsoid
Eigenvectors of Q are ellipsoid axes
Eigenvalues of Q are apparent diffusion coefficients (ADC) along these axes
  mean diffusion distance in time t =√(2λit)‏

## Slide 38: Diffusion Probes Microscopic Structures In the Brain
H2O
Unimpeded direction- large ADC
Impeded direction- smaller ADC
White matter fibres
H2O
Principal axis is likely to be aligned with a fibre; Apparent Diffusion Coefficients (ADCs) are measured in 6 directions

## Slide 39: Diffusion Imaging
“The success of diffusion MRI is deeply rooted in the powerful concept that during their random, diffusion driven displacements molecules probe tissue structure at a microscopic scale well beyond the usual image resolution: during typical diffusion times of about 50 msec”
The only non-invasive measurement of diffusion
Doesn’t interfere with diffusion
The diffusion is an intrinsic process; diffusion does not depend on the distortions introduced into the local magnetic field; hence it is unlike the T1 or T2 effects

## Slide 40: DTI Reveals White Matter Structure
Anisotropy
Principal Direction
Mean Diffusivity

## Slide 41: Fractional Anisotropy (Basser & Pierpaoli, 1996)‏
Normalized variance of ellipsoid axis magnitudes
  FA=0 for sphere
  FA=1 for tube
  FA is dimensionless
Notes: If full tensor data acquisition is applied, the Fractional Anisotropy is calculated from the eigenvalues l1, l2, l3 of the diffusion tensor:
where l is the mean diffusivity (trace/3).
FA=0 for sphere (l=[1,1,1])‏
FA=1 for 'infinitely long cigar (l=[1,0,0])‏
FA=.71 (sqrt(2)/2) for infinitely flat pancake (l=[1,1,0])‏
in matlab:
fa = sqrt(3)/sqrt(2)*sqrt((l(1)-mean(l))^2 + (l(2)-mean(l))^2 + (l(3)-mean(l))^2)/sqrt(sum(l.^2))‏

## Slide 42: Diffusion Anisotropy in Celery FA is not a reliable indicator of myelination
b (s/cm2)‏
Spin-echo amplitude (arbitrary units)‏
parallel
perpendicular
t1-weighted
DTI
from Numano et. al., MRI 2006
FA ~0.3 in vascular bundles of celery
from Beaulieu, NMR Biomed 2002
Notes: (Celery MR images) Fig. 3. T1-weighted anatomy (left) and color-coded V1 map (right) of fresh celery. To facilitate the visualization of vascular bundle orientation, only the area where the FA value exceeded 0.27 is displayed. Water molecules inside the vascular bundle were highly directional along the celery branch (arrow).

## Slide 43: Diffusion Tensor Imaging (Le Bihan et al.)
White matter properties that influence the apparent diffusion coefficient
density of fibers
degree of myelination
average fiber diameter
directional similarity of the fibers in the voxel.

## Slide 44: DW Tractography
Helps interpretation of statistical maps
Useful for finding precise locations of know tracts (e.g., presurgical planning)‏
May be useful for discovering unknown tracts (connectome analysis)‏
Useful for generating white matter ROIs
Makes pretty pictures

## Slide 45: Trace paths through the tensors
Principal Diffusion Direction (PDD)- longest axis of the diffusion ellipsoid (unit vector)‏
Assume PDD is tangent to fiber tract (deterministic) or create a PDF of tangents (probabilistic)
Estimate path integrals
diffusion tensor
principal diffusion direction (PDD)‏

## Slide 46: Occipital Fibers
1cm scale bars

## Slide 47: Occipital Callosal Fibers
1cm scale bars

## Slide 48: Occipital Callosal Fibers
1cm scale bars

## Slide 49: Segmenting the Corpus Callosum
Lateral Ventricle
Corpus Callosum

## Slide 50: Callosal Segments in 49 Children

## Slide 51: Probabilistic Tractography
Treat PDD as a PDF rather than an axis
Generate many pathways according to PDD PDFs and anatomical constraints
Discard 'bad' pathways
Infer something about the brain
Optic radiation estimated with Behren's FDT in FSL (from Jbabdi et. al. 2007)‏

## Slide 52: Connection-based Tractography (ConTrack, Sherbondy et. al., Journal of Vision, 2008)‏
Find the best pathways connecting two regions
Create ROIs
Sample many pathways
Score & threshold pathways

## Slide 53: ConTrack produces better estimates of the optic radiation
D
C
FDT OR estimates
New FDT algorithm (Jbabdi)‏
ConTrack OR estimates

## Slide 54: Quantitative comparison with gold-standard dissection Sherbondy, Dougherty, Napel & Wandell (2008) JOV
E
D
C
B
Occipital pole (OP)‏
Temporal pole (TP)‏
Meyer’s Anterior (MA)‏

## Slide 55: ConTrack OR pathways closely match gold-standard
B
E
C
D
Sherbondy et. al. (2008) JOV.

## Slide 56: Both deterministic and probabilistic algorithms can fail
Jones 2008, Fig. 10 – Example of reproducible, but artefactual reconstructions. (A) shows the individual streamlines reconstructed as part of the probabilistic algorithm, originated from the single seedpoint indicated by the star. (B) Shows the voxel-intersection maps thresholded at ‡1%. In both (A) and (B), the most visited path after passing inferiorly from the seedpoint is across the pons and up the contralateral cortico-spinal tract. (C) Shows that thresholding at ‘high’ conﬁdence (‡50% intersection) removes these false positive reconstructions.

## Slide 57: HARDI to the rescue!