## Slide 1
Magnetic resonance methods
Neurobiology 206
Wandell
Source of noise
Walter K.

## Slide 2: Neuroscience and clinical neuroimaging

## Slide 3: Neuroscience and clinical data span a huge range of spatial and temporal resolution.
Structural MRI
Notes: fmri-fig-01-07-0.jpg

## Slide 4: Neuroscience techniques differ in their spatial resolution, temporal resolution, and invasiveness
Functional Magnetic Resonance Imaging, Huettel et al. © Sinauer, 2004, 2009
Notes: huettel-2e-fig-01-08-0.jpg

## Slide 5
MR: The instrument

## Slide 6: A modern MRI scanner.
B0
RF
Notes: fmri-fig-01-02-0.jpg

## Slide 7: The steady-state (B0) field
In the MR scanner, there is a uniform field (1.5-9T)
The uniform field is about 40 cm (head is about 25 cm)
The precision of the constant field is precise to about 2 parts per million
B0 establishes an oriented lowest energy state for the protons

## Slide 8: The B0 Field
Magnetic Flux Density (magnetic field per unit time per unit area). Standard International Units: Tesla
Tesla = 10,000 Gauss
Earth’s magnetic field: 0.5G; Refrigerator magnet 200 Gauss
MR Magnet strengths 1.5 - 9T (15,000 G – 90,000 G)
Nikolas Tesla
Johan Carl Friedrich Gauss

## Slide 9: The free induction decay experiment
Beaker of water in a perfectly uniform magnetic field
RF signal excites spins
Bloch
Purcell
Measured voltage signal
Coil
Notes: http://www.youtube.com/watch?v=MPXbDDRumwM

## Slide 10: The FID signal: quantal description
B0 field precession
In the presence of the B0 field, the spins generally align with the field (Z-direction)
But they occupy one of two states: Parallel and anti-parallel
(mrTutMR.m explains how to calculate the percentage in each state)
Functional Magnetic Resonance Imaging, Huettel et al. © Sinauer, 2004, 2009
Z
Parallel
Anti-parallel
Hydrogen nuclei (protons) are called spins in MR
Notes: The protons oscillate between one of two permissible states. The energy difference between these two states determines the frequency of an RF signal that is needed to flip from one state to the other. This is called the Larmor frequency. Slightly more of the protons have their positive side (red) oriented along with the B0 field. If we add an RF pulse along the longitudinal axis at this frequency, we change the preponderance of the spins from the orange state to the blue state. They will then relax back along the main axis

## Slide 11: FID: The bulk (net) magnetization metaphor
The bulk magnetization precesses around the B0 axis. Radio frequency (RF) pulse changes the angle of the bulk magnetization. When the RF stops, the spins recover to the low energy state.
Receiver coil measures the spins as their net transverse magnetization decays; this transverse decay is the only signal we measure.
Low energy state in the B0 field
Functional Magnetic Resonance Imaging, Huettel et al. © Sinauer, 2004, 2009
Notes: Figure 3.4 Precession. The movement of a rotating proton or magnet within a magnetic
field (A) is similar to the movement of a top in the earth’s gravitational field (B).
In addition to their spinning motion, their axis of spin itself wobbles around a vertical
axis; this motion is known as precession.

## Slide 12: The RF signal causes the bulk magnetization to precess around the main axis
Functional Magnetic Resonance Imaging, Huettel et al. © Sinauer, 2004, 2009
Notes: Figure 3.4 Precession. The movement of a rotating proton or magnet within a magnetic field (A) is similar to the movement of a top in the earth’s gravitational field (B). In addition to their spinning motion, their axis of spin itself wobbles around a vertical axis; this motion is known as precession.

## Slide 13: The RF signal measured in MR
The receiver coil picks up the changing magnetic field caused by the changing magnetization in the transverse plane.
Receiver
Functional Magnetic Resonance Imaging, Huettel et al. © Sinauer, 2004, 2009
Transverse magnetization is the only signal we measure.
Notes: Figure 3.16 MR signal reception. As the net magnetization rotates through the transverse plane, the amount of magnetic flux experienced by the receiver coil changes over time (A and B). The changing flux generates an electromotive force, which provides the basis for the MR signal.

## Slide 14: The RF signal size varies with its angle from the transverse plane
The duration of the RF pulse controls the bulk precession angle
Short RF pulse
Long RF pulse

## Slide 15: Mechanisms of MR signal decay
Spin-lattice (T1)
Spin-spin interactions (T2)
(There are others, not discussed)
Notes: susceptibility
Definition: (1) magnetic susceptibility - Symbol cm. The dimensionless quantity describing the contribution made by a substance when subjected to a magnetic field to the total magnetic flux density present. It is equal to mr-1, where mr is the relative permeability of the material. Diamagnetic materials have a low negative susceptibility, paramagnetic materials have a low positive susceptibility and ferromagnetic materials have a high positive value.

## Slide 16: The bulk magnetization is the sum of two components
z
x
y
=
+
Precessing
spin
Longitudinal
component
Transverse
component

## Slide 17: Longitudinal relaxation (T1)
Time
RF pulse
x
y
z
4 sec
Suppose we apply a pulse that flips the bulk magnetization 180 deg. The longitudinal recovery follows an exponential time course, with a constant called T1
Notes: The net magnetization is shown at several points. The first is the magnetization in the steady B0 field. Then, an RF pulse at the Larmor frequency is introduced. This flips the net magnetization along the Z-axis. Then, over time, the net magnetization returns to the steady state position.

## Slide 18: Longitudinal relaxation rate depends on your neighborhood
The T1 values of water located in different brain tissue vary.
At 1.5T a good time to measure for contrast is around 0.8-1.2 sec following the RF pulse.
Time (s)
0
1
2
3
4
5
6
0
0.2
0.4
0.6
0.8
1
Longitudinal magnetization (Mz)
Gray
White
Gray (T1,G): 0.88 s
White (T1,W): 0.65 s
Notes: The time course of the net magnetization depends on the material. So, if we measure the magnetic field strength, say, one second after a pulse, a container with water will have a lower magnetization than a container with lipids. This difference, based on the biochemical structure of the material, is the basis for seeing different components of the brain (CSF, gray matter, white matter).

## Slide 19: The difference between gray and white signals at different times
At 1.5T a good time to measure is around 0.8 sec following the RF pulse.
0
2
4
6
0
0.02
0.06
0.1
Time (s)
Magnetization difference
Notes: The time course of the net magnetization depends on the material. So, if we measure the magnetic field strength, say, one second after a pulse, a container with water will have a lower magnetization than a container with lipids. This difference, based on the biochemical structure of the material, is the basis for seeing different components of the brain (CSF, gray matter, white matter).

## Slide 20: The T1-contrast distinguishes gray and white matter
T1 Anatomical
Sagittal
Axial
Coronal
T1-weighted images are typically used for understanding gray matter atrophy, or ventricular enlargement
Notes: The time course of the net magnetization depends on the material. So, if we measure the magnetic field strength, say, one second after a pulse, a container with water will have a lower magnetization than a container with lipids. This difference, based on the biochemical structure of the material, is the basis for seeing different components of the brain (CSF, gray matter, white matter).

## Slide 21: Transverse magnetization
x
y
Field-free space
B0 field
Following
RF Pulse
x
y
RF pulse

## Slide 22: Transverse relaxation: T2
RF pulse
Time
200 ms
Red arrows denote individual spins
Bulk transverse magnetization follows an exponential recovery with a time constant called T2

## Slide 23: Selection of TR and TE values for T1 contrast.
The T2 time constant is much shorter than T1. Consider the practical aspects.
Notes: fmri-fig-05-05-2.jpg

## Slide 24: T2 images
T2-weighted images measure pathologies involving fluid filled regions (tumors, arterio-veinous malformations, edema)
AVM

## Slide 25: Summary of terms
Bulk magnetization
Transverse and longitudinal magnetization
B0 field = Main magnetic field
T1 = longitudinal recovery time
T2 = transverse decay time
RF = Radio frequency pulse (B1)
TR = Time between two RF pulses
TE = Time from RF pulse to peak of signal induced in the coil
Tesla = Unit of magnetic field strength (10,000 Gauss)

## Slide 26: A sample magnetic resonance angiography (MRA) image.
Magnetic resonance angiography is valuable for identifying cardio-vascular problems and complications from stroke.
Spin-saturation within a plane removes the static signals. Spins that stay within a plane remain saturated and produce no contrast. Blood moves between planes and is detected (not saturated).
Notes: fmri-fig-05-12-0.jpg

## Slide 27: Functional MRI Signals
Blood Oxygen Level Dependent (BOLD) signals

## Slide 28: Neural and vascular activity are coupled
Source of noise
Walter K.
Operation
On turning down a left occipital bone flap,a large angry-looking angioma arteriale racemosum of the left occ. Lobe was disclosed which extensively involved the visual cortex. The haemorrhage occasioned by the bone flap was so excessive that the operation had to be abandoned without touching the tumour. A decompression, however, was made. The patient was discharged … with greatly improved vision.
Observations Upon the Vascularity of the Human Occipital Lobe During Visual Activity
J.F. Fulton, M.D. (1928)
Notes: Observations Upon the Vascularity of the Human Occipital Lobe During Visual Activity

## Slide 29: Neural and vascular activity are coupled
Subject noted that ‘the noise in the back of his head increased in intensity when he was using his eyes.’
No increase for hearing, touch or smell
Increased more when he tried harder
Instruments
Source of noise
Walter K.
Observations Upon the Vascularity of the Human Occipital Lobe During Visual Activity
J.F. Fulton, M.D. (1928)
Notes: Observations Upon the Vascularity of the Human Occipital Lobe During Visual Activity

## Slide 30: Blood oxygenation increase is localized
Sokolow
Raichle
Fox
Notes: Figure 2

## Slide 31: Blood oxygenation influences T2
Time
Deoxygenated
Oxygenated
(Huettel et al., Fig 7.1; After Thulborn, 1982)
Notes: Figure 7.1 Effects of blood deoxygenation upon MR relaxation constants. Shown are the differential effects of blood deoxygenation upon transverse and longitudinal relaxation times, as expressed by the constants 1/T2 (blue circles) and 1/T1 (red circles). The xaxis indicates the square of the proportion of deoxygenated blood. Note that oxygenation increases from left to right. Clearly evident is the fact that 1/T2 decreases with increasing oxygenation; that is, the more deoxygenated hemoglobin that is present, the shorter the T2. Note that T1 is not affected by blood oxygenation level. (After Thulborn et al., 1982.)

## Slide 32: Human Vasculature Inhomogeneities: (Duvernoy)
There is a lot of it

## Slide 33: Main energy cost: maintain and restore ionic potentials at the synapse
Sub-threshold synaptic potentials
Action potentials (spikes)
Huettel et al. calls this ‘integrative and signaling roles’ of neurons

## Slide 34: Energy budget estimate
Figure after Huettel et al.
D. Attwell and S.B. Laughlin, An energy budget for signaling in the grey matter of the brain. J. Cereb. Blood Flow Metab. 21 (2001), pp. 1133–1145.
Spike restoration
Sub-threshold restoration
Steady-state

## Slide 35: fMRI may complement or replace more invasive, costly, and dangerous tests
The Wada test (Wada and Rasmussen, 1960)
Behavioral testing after the injection of an anesthetic into the right or left internal carotid artery. Depending on how the injection is made (and the quantity), there is some time during which activity in one of the cerebral hemispheres is suspended. During this time, the abilities subserved by the other hemisphere can be tested in isolation.
Typical uses of the test include the lateralization of language abilities (the surgeon wants to know if the hemisphere being operated on is the speech hemisphere or not), and a determination that the person will not be amnesic after surgery.
Juhn Wada
Notes: http://www.neuro.mcg.edu/np/INS%20Wada%20Syllabus.htm

## Slide 36: fMRI may replace more invasive, costly, and dangerous tests
Is the Wada safe?
A Wada test is generally a safe procedure with very few risks. There is a small risk of certain complications ranging from pain where the catheter is inserted to stroke.
The risk of stroke is less than 1% overall. It is greater, but still relatively low, if you are older or if you have atherosclerosis (hardening of the arteries) or a history of high cholesterol.
The Wada has often been used in pre-surgical testing for epilepsy, not a life-threatening condition. Hence, a 1% morbidity rate is significant.
Juhn Wada
Notes: http://www.neuro.mcg.edu/np/INS%20Wada%20Syllabus.htm

## Slide 37: Example of fMRI applied to pre-surgical planning: Replacing Wada testing
Use of preoperative functional neuroimaging to predict language deficits from epilepsy surgery. Sabsevitz DS, Swanson SJ, Hammeke TA, Spanaki MV, Possing ET, Morris GL 3rd, Mueller WM, Binder JR. Department of Neurology and the Comprehensive Epilepsy Center, Medical College of Wisconsin, Milwaukee 53226, USA.
BACKGROUND: Left anterior temporal lobectomy (L-ATL) may be complicated by confrontation naming deficits. OBJECTIVE: To determine whether preoperative fMRI predicts such deficits in patients with epilepsy undergoing L-ATL. METHODS: Twenty-four patients with L-ATL underwent preoperative language mapping with fMRI, preoperative intracarotid amobarbital (Wada) testing for language dominance, and pre- and postoperative neuropsychological testing. fMRI laterality indexes (LIs), reflecting the interhemispheric difference between activated volumes in left and right homologous regions of interest, were calculated for each patient. Relationships between the fMRI LI, Wada language dominance, and naming outcome were examined. RESULTS: Both the fMRI LI (p < 0.001) and the Wada test (p < 0.05) were predictive of naming outcome. fMRI showed 100% sensitivity and 73% specificity in predicting significant naming decline. Both fMRI and the Wada test were more predictive than age at seizure onset or preoperative naming performance. CONCLUSIONS: Preoperative fMRI predicted naming decline in patients undergoing left anterior temporal lobectomy surgery.
Pre-surgical measurements of left lateralization predict the post-surgical performance

## Slide 38
Medina et al., 2007 L.S. Medina, B. Bernal and J. Ruiz, Role of functional MR in determining language dominance in epilepsy and nonepilepsy populations: a Bayesian analysis, Radiology 242 (2007), pp. 94–100.Full Text via CrossRef | View Record in Scopus | Cited By in Scopus (4)

## Slide 39: References on fMRI applications in the clinic
Functional MRI Predicts Postsurgical Memory following Temporal Lobectomy
Rabin ML, Narayan VM, Kimberg DY, Casasanto DJ, Glosser G, Tracy JI, French JA, Sperling MR, Detre JA
Brain 2004;127:2286–2298 [PubMed] [Full Text].
Pre-operative Verbal Memory fMRI Predicts Post-operative Memory Decline after Left Temporal Lobe Resection
Richardson MP, Strange BA, Thompson PJ, Baxendale SA, Duncan JS, Dolan RJ
Brain 2004;127:2419–2426 [PubMed] [Full Text].
http://www.pubmedcentral.nih.gov/articlerender.fcgi?artid=1201639
How Close is fMRI to Providing the Memory Component of the Wada Test?
Bassel W Abou-Khalil, MD
Epilepsy Curr. 2005 September; 5(5): 184–186.
doi: 10.1111/j.1535-7511.2005.00058.x.
Copyright 2005 by the American Epilepsy Society

## Slide 40: Diffusion tensor imaging and fiber tractography of human brain pathways
Notes: This is a picture from a new algorithm we have developed that tracks fibers into regions that have been difficult to follow. Don’t talk about it yet because it’s too complicated – even for me.

## Slide 41: Human fiber tracts
Courtesy Professor Ugur Ture

## Slide 42: White Matter Growth
Age (years)
Aspects of the white matter are thought to still be developing into teenage years
Notes: Brain Research Bulletin Volume 54, Issue 3 , February 2001, Pages 255-266

## Slide 43: Diffusing Water Probes Microscopic Tissue Structure
Tissue structures affect diffusion
MR diffusion measures depend on microscopic structure within voxel
Diffusion through white matter probes:
  density of axons
  degree of myelination
  average fiber diameter
  directional similarity of axons

## Slide 44: Over time, molecules within gases or liquids move through the medium

## Slide 45: In a complex tissue, there is both isotropic and anisotropic diffusion

## Slide 46: Diffusion probes brain microscopic structure
Along the axon, within the cytoskeleton, there is a large Apparent Diffusion Coefficient (ADC)
Optic nerve fibres
George Bartzokis
Longitudinal Diffusivity (μm2/ms)
Notes: Lets examine another microscopic picture of an ideal fascicle chunk of tissue to get an explanation for the correlation between fascicle orientation and direction of maximal diffusion. Along the length of the axon bundle, the water molecules mostly travel through the cytoskeletal fluid of the axons and have a large diffusivity constant. We name this the longitudinal diffusivity. Which we often discuss in the units of microns squared / ms.

## Slide 47: H2O diffusion probes microscopic structure of the brain
Bi-lipid cell membranes limit diffusion.
Hence, perpendicular to the length the ADC is smaller
Radial Diffusivity (μm2/ms)
Optic nerve fibres
George Bartzokis
Notes: Perpendicular to the length of the fascicle however, the water molecules face many more obstacles due to myelin insulation around axons and the tight packing of the coherent axons within the fascicles. This smaller diffusivity constant is termed radial diffusivity.

## Slide 48: DTI summarizes data
The mean distance that a typical water molecule will diffuse in a unit of time
Notes: Now lets perform a DTI scan of this ideal fascicle chunk of tissue. If we would scan along the longitudinal axis, we measure this large diffusion constant here. Then in a radial direction we would get this radial diffusivity here. And further directions we would receive some combination of the two diffusion amounts. And we may try to model such a diffusion surface as an ellipsoid here, otherwise known as a tensor. Note that the surface has a special meaning as the mean distance a typical…

## Slide 49: Potential Applications: Monitoring Cognitive Development
Dyslexia is a neuro-developmental learning disability
One hypothesis is that this disability involves disruption of the white matter (disconnection syndrome)
Potential applications: Autism, Multiple Sclerosis, Epilepsy
Diffusion tensor imaging is one of the few ways to characterize human white matter; it is the only in vivo method.

## Slide 50: DTI Fiber Tracking (DTI-FT)
Conventional MR volumes are real-valued
DTI data are surfaces
Notes: First, lets contrast the DTI output image to the T1 image I showed earlier. Note, that both measurements have voxels or volume measurements of the tissue at many 3D locations. However, unlike conventional MRI, each DTI measurement is a diffusion surface rather than a single value. In the T1 data, one may attempt to reverse engineer or segment tissue components by grouping similar contiguous intensity values. One can argue that fascicle estimation has a similar aim in that we are attempting to group similar and contiguous diffusion surfaces as shown here as we track along anisotropic voxels heading in a consistent direction.
However, we just saw that reverse engineering some voxels leaves infinitely many equally likely solutions. This is what mathematicians call an ill-posed problem. Now imagine that if we cannot perfectly recover the source for diffusion at one location what hope do we have for the entire brain.

## Slide 51: MRI: the only noninvasive white matter measurement
Courtesy Professor Ugur Ture
Signals between widely separated gray matter regions are carried by long fibers called white matter
Scientists have learned how to measure these fibers in the living human brain using Diffusion tensor imaging

## Slide 52: Learning and reading disabilities
Some fibers are important for specific tasks, such as reading, language, or math. Damage to the fibers shown produces specific reading deficits.
Proper fiber development is essential for good cognitive functioning.
Corpus
callosum
Ventricle
Fibers
Gray matter
White matter
Dougherty, Ben-Shachar, Bammer, Brewer & Wandell (2005)
Proceedings of the National Academy of Sciences USA

## Slide 53: Radial diffusivity in callosum that projects to temporal lobes correlates with sounding out words (Dougherty et al., PNAS, 2007)
Reading-related scores
O
P
S
T
T

## Slide 54: Acquired alexia: Callosal Lesion
L
R
Mao-Draayer & Panitch (2004), Alexia without agraphia in multiple sclerosis...
Notice the series of places with a lesion. Are these multiple white matter locations, or does this reflect degeneration within a single fiber tract?
Notes: Figure 1 Axial and sagittal fluid attenuation inversion recovery (FLAIR) MRI demonstrates lesions in the splenium of the corpus callosum (A and B) and the left occipital WM adjacent to the occipital horn of the lateral ventricle (C).
Alexia without agraphia in multiple sclerosis: case report with magnetic resonance imaging localization
Yang Mao-Draayer and Hillel Panitch
Department of Neurology, University of Vermont College of Medicine, Burlington, VT, USA
Multiple Sclerosis (2004) 10, 705 /707
The syndrome of alexia without agraphia occurs rarely in multiple sclerosis (MS). We report a patient with right homonymous hemianopsia and alexia without agraphia as his initial manifestations of relapsing / remitting MS. Magnetic resonance imaging (MRI) demonstrated a hyperintense lesion in the left occipital subcortical white matter (WM) and an enhancing lesion in the splenium of the corpus callosum. The clinical presentation and MRI findings were consistent with disconnection of the functional right occipital visual cortex from structures responsible for language comprehension in the left hemisphere. The diagnosis of MS was confirmed by subsequent development of additional periventricular WM lesions.

## Slide 55: Forceps lesion location (average brain)
Locate positions of the lesion in the forceps within a template of 20 brains.
R
L
R
L
Subject
Template of 20 subjects
Notes: Figure 1 Axial and sagittal fluid attenuation inversion recovery (FLAIR) MRI demonstrates lesions in the splenium of the corpus callosum (A and B) and the left occipital WM adjacent to the occipital horn of the lateral ventricle (C).
Alexia without agraphia in multiple sclerosis: case report with magnetic resonance imaging localization
Yang Mao-Draayer and Hillel Panitch
Department of Neurology, University of Vermont College of Medicine, Burlington, VT, USA
Multiple Sclerosis (2004) 10, 705 /707
The syndrome of alexia without agraphia occurs rarely in multiple sclerosis (MS). We report a patient with right homonymous hemianopsia and alexia without agraphia as his initial manifestations of relapsing / remitting MS. Magnetic resonance imaging (MRI) demonstrated a hyperintense lesion in the left occipital subcortical white matter (WM) and an enhancing lesion in the splenium of the corpus callosum. The clinical presentation and MRI findings were consistent with disconnection of the functional right occipital visual cortex from structures responsible for language comprehension in the left hemisphere. The diagnosis of MS was confirmed by subsequent development of additional periventricular WM lesions.

## Slide 56: Application of DTI
Find the fiber paths in the template that pass through the lesion
Locate where these paths pass through the corpus callosum.

## Slide 57: Fiber tracts predict lesion location in callosum
Predicted location of lesioned fiber in template
Observed lesion in patient
Notes: Figure 1 Axial and sagittal fluid attenuation inversion recovery (FLAIR) MRI demonstrates lesions in the splenium of the corpus callosum (A and B) and the left occipital WM adjacent to the occipital horn of the lateral ventricle (C).
Alexia without agraphia in multiple sclerosis: case report with magnetic resonance imaging localization
Yang Mao-Draayer and Hillel Panitch
Department of Neurology, University of Vermont College of Medicine, Burlington, VT, USA
Multiple Sclerosis (2004) 10, 705 /707
The syndrome of alexia without agraphia occurs rarely in multiple sclerosis (MS). We report a patient with right homonymous hemianopsia and alexia without agraphia as his initial manifestations of relapsing / remitting MS. Magnetic resonance imaging (MRI) demonstrated a hyperintense lesion in the left occipital subcortical white matter (WM) and an enhancing lesion in the splenium of the corpus callosum. The clinical presentation and MRI findings were consistent with disconnection of the functional right occipital visual cortex from structures responsible for language comprehension in the left hemisphere. The diagnosis of MS was confirmed by subsequent development of additional periventricular WM lesions.

## Slide 58: Summary
MR contrast mechanisms
  T1 anatomical contrast
  T2 edema, AVM
Functional MRI (fMRI, BOLD)
  Blood oxygen, synaptic signaling
  Predictive cognitive surgical outcomes
Diffusion tensor imaging
  White matter tracts
  Analyze brain development and connectivity
  Predict cognitive performance

## Slide 59
Extra

## Slide 60: Understanding the developing child’s brain
Projection zones

## Slide 61: Learning and reading disabilities
Projection zones
All callosal fibers
Regions of interest
Segmented fibers

## Slide 62: Learning and reading disabilities
Projection zones
Anterior commisure

## Slide 63: Understanding the developing child’s brain
Recurring tumor in the brain (5 years old)
Irradiated entire brain; radiation-induced necrosis
Inventory pathways in controls
Assess missing pathways
Time of radiation implies which pathways are growing
What if a child is missing a pathway? What can we expect of them
Directed radiation – gamma knife
Radiation necrosis

## Slide 64: Pluses and minuses of fiber tractography
Functional organization of human occipital-callosal fiber tracts Robert F. Dougherty, Michal Ben-Shachar, Roland Bammer, Alyssa Brewer, Brian Wandell (2005). PNAS, v. 102, no. 20, pp. 7350-7355.

## Slide 65: Human fiber tracts and reading
From: The Virtual Hospital (www.vh.org); TH Williams, N Gluhbegovic, JY Jew

## Slide 66: Diffusion Probes Microscopic Structures In Brain Tissue
H2O
Unimpeded direction- large ADC
Impeded direction- smaller ADC
White matter fibres
H2O
Principal axis is likely to be aligned with a fibre; Apparent Diffusion Coefficients (ADCs) are measured in 6 directions

## Slide 67: Fractional Anisotropy: (Basser & Pierpaoli, 1996)
Normalized variance of ellipsoid axis magnitudes
  FA=0 for sphere
  FA=1 for tube
Notes: If full tensor data acquisition is applied, the Fractional Anisotropy is calculated from the eigenvalues l1, l2, l3 of the diffusion tensor:
where l is the mean diffusivity (trace/3).
FA=0 for sphere (l=[1,1,1])
FA=1 for 'infinitely long cigar (l=[1,0,0])
FA=.71 (sqrt(2)/2) for infinitely flat pancake (l=[1,1,0])
in matlab:
fa = sqrt(3)/sqrt(2)*sqrt((l(1)-mean(l))^2 + (l(2)-mean(l))^2 + (l(3)-mean(l))^2)/sqrt(sum(l.^2))

## Slide 68: DTI Reveals Differences In White Matter Structure
T1
DTI: Fractional Anisotropy

## Slide 69: We Confirmed This Correlation In Children and Adults
r = 0.78
(p = 0.01)
Adults
Children (8-12)
r = 0.62
(p = 0.017)
Children's Reading Performance is Correlated with White Matter Structure Measured by Diffusion Tensor Imaging Gayle K. Deutsch, Robert F. Dougherty, Roland Bammer, Wai Ting Siok, John D.E. Gabrieli, Brian Wandell (2005). Cortex, v. 41, pp. 354-363.
Poor readers
Normal readers
Notes: All Stanford students. Two red marks are subjects who claimed to be ‘dyslexic’ (“compensated” dyslexics?). FA accounts for 61% of the reading variance!

## Slide 70: What More Can We Learn From Principal Diffusion Direction (PDD)?
Fractional Anisotropy = 0.6
Principal Diffusion Directions differ
There is more information to be analyzed

## Slide 71: Using Direction We See Much More
Accounting for Directional Data Requires New Statistical Methods
(Schwartzmann, Dougherty, Taylor, 2005, MRM)

## Slide 72: Can We Understand All of These Data By Analyzing Fiber Tracts (DTI-FT)?
Many interesting algorithm issues
Algorithm thresholds (direction, FA)
Confidence intervals, probabilistic reasoning
Spatial sampling
  Samples are sparse, but directions are fine
  Interpolation to intermediate positions
Spatial co-registration between modalities (T1, fMRI) and subjects
Validation needed